## Slide 1: Computer Architecture 计算机体系结构
School of Computer and Information Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 6: Chapter 3. Pipelining 流水线

## Slide 7
3.1 What is Pipelining
3.2 The Basic Pipelining for DLX
3.3 The Major Hurdle of Pipelining
3.4 Data Hazards
3.5 Control Hazards
3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Chapter 3 Pipelining

## Slide 8
3.7 Overcoming Data Hazards with Dynamic Scheduling
3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
3.9 Taking Advantage of More ILP with Multiple Issue
Chapter 3 Pipelining

## Slide 9: 3.1 What is Pipelining
Example:
小明, 小红, 李华, 韩梅梅 to wash, dry, and fold;
洗衣店1：
Washer takes 30 minutes
Dryer takes 30 minutes
Folder takes 30 minutes
A
B
C
D

## Slide 10: 3.1 What is Pipelining
洗衣店用 6小时完成了4个任务（0.67t/h）；
4个同学各等待了1.5小时；
Washer使用2小时（0.33)；Dryer使用2小时（0.33) ；Folder使用2小时（0.33) ；
C
任
务
顺
序
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
Midnight
D
B
A

## Slide 11: 3.1 What is Pipelining
洗衣店用3小时完成了4个任务（1.33t/h）；
4个同学各等待了1.5小时；
Washer使用2小时（0.66)；Dryer使用2小时（0.66) ；Folder使用2小时（0.66)；
任
务
顺
序
6 PM
7
8
9
10
Midnight
30
30
30
30
30
30
A
B
C
D

## Slide 12: 3.1 What is Pipelining
小明, 小红, 李华, 韩梅梅 to wash, dry, and fold;
洗衣店2：
Washer takes 30 minutes
Dryer takes 40 minutes
Folder takes 20 minutes
A
B
C
D

## Slide 13: 3.1 What is Pipelining
洗衣店用 6小时完成了4个任务（0.67t/h）；
4个同学各等待了1.5小时；
Washer使用2小时（0.33)；Dryer使用2小时40分（0.44) ；Folder使用1小时20分（0.22) ；
A
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
B
C
D
任
务
顺
序

## Slide 14: 3.1 What is Pipelining
洗衣店用3.5小时完成了4个任务（1.14t/h）；
4个同学各等待了1.5小时；
Washer使用2小时（0.57)；Dryer使用2小时40分（0.76) ；Folder使用1小时20分（0.38) ；
A
B
C
D
任
务
顺
序
6 PM
7
8
9
10
11
Midnight
30
40
40
40
40
20

## Slide 15: 3.1 What is Pipelining
流水线不能缩短单个任务的响应时间，但可以提高吞吐率；
流水线速度限制于最慢流水站的速度；
流水线中多个任务是并行处理的；
最大加速比 = 流水站数
30
40
40
40
40
20

## Slide 16: 3.1 What is Pipelining
将一重复的时序过程分解为若干子过程，每个子过程都可有效地在其专用功能段上与其它子过程同时执行，这种技术称为流水技术。
Pipelining: is an implementation technique whereby multiple instructions are overlapped in execution.多指令重叠运行
Different steps are completing different parts of different instructions in parallel. 不同步骤并行完成不同指令的不同部分
Each step is called: pipe stage or pipe segment. 流水段

## Slide 17: 3.1 What is Pipelining
时空图：从时间和空间两个方面描述流水线的工作过程，横坐标表示时间，纵坐标表示各流水段

## Slide 18: 3.1 What is Pipelining
Throughput of an instruction pipeline (流水线的吞吐量): how often an instruction exits the pipeline
Machine cycle (机器周期): the time required between moving an instruction one step down the pipeline. 指令在流水线移动一步所需时间
  Because all stages proceed at the same time, the length of a machine cycle is determined by the time required for the slowest pipe stage. 由最慢的流水线段决定
  is usually one clock cycle (sometimes it is two, rarely more). 通常是一个时钟周期，有时是两个，很少是更多个

## Slide 19: 3.1 What is Pipelining
The Goal of pipeline designer: balance the length of pipeline stages. 平衡流水段的长度
If perfectly balanced, time per instruction on the pipeline machine is:
Optimum speedup from pipelining equal the number of pipe stages.
Usually, optimum is not achieved for:
  not be perfectly balanced. 不能完全平衡
  pipelining overhead. 流水线开销，流水线“填充”和“排空”时间

## Slide 20: 3.1 What is Pipelining
加速比：
假设为m段流水线，共n个任务，则加速比为？

## Slide 21: 3.1 What is Pipelining

## Slide 22: 3.1 What is Pipelining
Improvement can be viewed as:
  decreasing CPI ( if multiple clock cycles per instruction). 降低CPI
  decreasing the clock cycle time (one long clock cycle per instruction). 降低时钟周期
  combination.
  Pipelining is an implementation technique that exploits parallelism among the instructions in a sequential instruction stream. It is not visible to the programmer (透明).

## Slide 23: 3.1 What is Pipelining
We will:
define five steps a DLX instruction involves. 首先定义DLX指令所涉及的5个步骤
implement DLX without pipelining. 再以无流水线的方式实现DLX
extend this implementation to a pipelined DLX. 再将该实现扩展成流水线DLX，与非流水对比
Every DLX instruction can be implemented in at most five clock cycles: IF, ID, EX, MEM, WB.
A Simple Implementation of DLX
DLX的一种简单实现

## Slide 24: 3.1 What is Pipelining

## Slide 25: 3.1 What is Pipelining----A Simple Implementation of DLX
1. Instruction fetch cycle (IF) 取指令:
Operation:
Send out the PC, fetch instruction from memory into instruction register (IR); 根据PC值从存储器中取出指令，并将指令送入指令寄存器IR
Increment the PC by 4 to address the next sequential instruction. PC值增加4，指向顺序的下一条指令
The IR hold the instruction that will be needed on subsequent clock cycles; IR中的指令将被执行
NPC is used to hold the next sequential PC.将下一条指令的地址放入临时寄存器NPC中
IR←Mem[PC]
NPC←PC+4

## Slide 26: 3.1 What is Pipelining----A Simple Implementation of DLX
1. Instruction fetch cycle (IF) 取指令:

## Slide 27: 3.1 What is Pipelining----A Simple Implementation of DLX
2. Instruction decode/register fetch cycle (ID)指令译码/读寄存器：
Operation:
Decode the instruction and access the register file to read the registers. 指令译码，读IR寄存器，按照寄存器号读寄存器文件
The outputs of the general-purpose registers are read into 2 temporary registers (A and B) for use in later clock cycles. 将读出结果放入两个临时寄存器A和B中
The lower 16 bits of IR are sign-extended and stored into temporary register Imm, for use in next cycle. 对IR寄存器中内容的低16位进行符号扩展，然后将符号扩展之后的立即值保存在临时寄存器Imm中
A←Regs[IR6..10]
B←Regs[IR11..15]
Imm←((IR16)16##IR16..31)

## Slide 28: 3.1 What is Pipelining----A Simple Implementation of DLX
2. Instruction decode/register fetch cycle (ID) 指令译码/读寄存器：

## Slide 29: 3.1 What is Pipelining----A Simple Implementation of DLX
2. Instruction decode/register fetch cycle (ID) 指令译码/读寄存器：
Thinking:
Why Instruction decode/register fetch parallel is possible? 为什么指令解码/寄存器取可并行进行？
  Fixed-field decoding: these fields are fixed. 固定域解码
  We may read a register we don’t use, which doesn’t help but also doesn’t hurt.
  Likely, the sign-extended immediate is also calculated during this cycle in case needed later, because the immediate portion of an instruction is located in an identical place in every DLX format.
A←Regs[IR6..10]
B←Regs[IR11..15]
Imm←((IR16)16##IR16..31)

## Slide 30: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX): 执行/有效地址计算
The ALU operates on the operands, performing 1 (of 4) function depending on instruction type. 根据指令类型进行四种操作之一
① Memory reference 存储器访问:
ALUoutput←A+Imm
Operation:
The ALU adds the operands to form the effective address and places result into register ALUOutput. 计算出有效地址，放到ALUOutput
LW R1, 100(R2) or SW R1, 100(R2)

## Slide 31: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
① Memory reference 存储器访问:

## Slide 32: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
② Register-Register ALU instruction 寄存器-寄存器ALU:
ALUoutput←A op B
Operation:
The ALU performs the operation specified by the function code on the value in A and B.
The result is placed in the temporary register ALUOutput.
ADD R1, R2, R3

## Slide 33: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
② Register-Register ALU instruction 寄存器-寄存器ALU:

## Slide 34: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
③ Register-Immediate ALU instruction 寄存器-立即数ALU:
ALUoutput←A op Imm
Operation:
The ALU performs the operation specified by the opcode on the value in A and in register Imm.
The result is placed in the temporary register ALUOutput.
ADD R1, R2, #3

## Slide 35: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
③ Register-Immediate ALU instruction 寄存器-立即数ALU:

## Slide 36: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
④ Branch 分支操作:
ALUoutput←NPC+Imm
Cond←(A op 0)
Operation:
The ALU do adds: NPC + Imm, to compute the address of the branch target. 计算目标地址
Register A is checked to determine whether the branch is taken. 检测A以确定是否转移
The comparison operation op is the relational operator determined by the branch opcode.
BEQZ R4, name

## Slide 37: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
④ Branch 分支操作:

## Slide 38: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX):执行/有效地址计算
Thinking:
Why effective address/execution can be combined into a single clock cycle? 为什么有效地址/执行可结合到一个时钟周期内？
Load-store architecture of DLX.
No instruction simultaneously calculate a data address, calculate an instruction target address, and perform an operation on the data. 没有指令在计算数据地址、目标地址的同时还对数据进行操作。

## Slide 39: 3.1 What is Pipelining----A Simple Implementation of DLX
4. Memory access/branch completion cycle (MEM):访存/分支操作完成
The only DLX instructions active in this cycle are loads, stores, and braches. 只有load、store和branch指令在这个周期活跃
① Memory reference: load and store 寄存器引用:
    LMD←Mem[ALUoutput] or
    Mem[ALUoutput]←B
Operation:
If is load, data returns from memory and is placed in the LMD (load memory data) register.
If is store, the data from B register is written into memory.
In either case the address used is computed during the prior cycle and stored in ALUOutput. 地址存在ALUOutput中, 已经在前一个周期计算出来

## Slide 40: 3.1 What is Pipelining----A Simple Implementation of DLX
4. Memory access/branch completion cycle (MEM):访存/分支操作完成
① Memory reference: load and store 寄存器引用:

## Slide 41: 3.1 What is Pipelining----A Simple Implementation of DLX
4. Memory access/branch completion cycle (MEM):访存/分支操作完成
② Branch 分支操作:
  if (Cond) PC←ALUoutput
  else PC←NPC
Operation:
If branches, PC is replaced with the branch destination address in register ALUOutput; 转移成功：转移目标地址送到PC
Otherwise, it is replaced with the incremented PC in the NPC. 转移不成功：NPC送到PC

## Slide 42: 3.1 What is Pipelining----A Simple Implementation of DLX
4. Memory access/branch completion cycle (MEM):访存/分支操作完成
② Branch 分支操作:

## Slide 43: 3.1 What is Pipelining----A Simple Implementation of DLX
5. Write-back cycle (WB) 写回:
① Register-Register ALU instruction寄存器-寄存器型ALU指令:
  Reg[IR16..20]←ALUoutput
Operation:
Write result into register file, whether it comes from memory (in LMD) or from ALU (in ALUOutput)
The register destination is dependent on function code.
② Register-Immediate ALU instruction寄存器-立即值型ALU指令:
  Reg[IR11..15]←ALUoutput
③ Load instruction load 指令:
  Reg[IR11..15]←LMD

## Slide 44: 3.1 What is Pipelining----A Simple Implementation of DLX
5. Write-back cycle (WB) 写回:
① Register-Register ALU instruction寄存器-寄存器型ALU指令:

## Slide 45: 3.1 What is Pipelining----A Simple Implementation of DLX
5. Write-back cycle (WB) 写回:
② Register-Immediate ALU instruction寄存器-立即值型ALU指令:

## Slide 46: 3.1 What is Pipelining----A Simple Implementation of DLX
5. Write-back cycle (WB) 写回:
③ Load instruction:

## Slide 47: 3.1 What is Pipelining----A Simple Implementation of DLX
 Figure: shows how an instruction flows through the datapath.

## Slide 48: 3.1 What is Pipelining----A Simple Implementation of DLX
 Figure: shows how an instruction flows through the datapath.

## Slide 49: 3.1 What is Pipelining----A Simple Implementation of DLX
Tips:
Storage is needed between stages:
store the value computed during a clock cycle.
required on a later clock cycle.
i.e., LMD, Imm, A, B, IR, NPC, ALUOutput, or Cond).

## Slide 50: Computer Architecture 计算机体系结构
School of Computer Science and Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 51: 3.1 What is Pipelining----A Simple Implementation of DLX
Tips:
Storage is needed between stages:
store the value computed during a clock cycle.
required on a later clock cycle.
i.e., A, B, IR, NPC, Imm, ALUOutput, LMD, or Cond.

## Slide 52: 3.1 What is Pipelining----A Simple Implementation of DLX
1. Instruction fetch cycle (IF) 取指令:
IR←Mem[PC]
NPC←PC+4
2. Instruction decode/register fetch cycle (ID)指令译码/读寄存器：
A←Regs[IR6..10]
B←Regs[IR11..15]
Imm←((IR16)16##IR16..31)

## Slide 53: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX): 执行/有效地址计算
① Memory reference 存储器访问:
ALUoutput←A+Imm
LW R1, 100(R2) or SW R1, 100(R2)
② Register-Register ALU instruction 寄存器-寄存器ALU:
ALUoutput←A op B
ADD R1, R2, R3

## Slide 54: 3.1 What is Pipelining----A Simple Implementation of DLX
3. Execution/effective address cycle (EX): 执行/有效地址计算
③ Register-Immediate ALU instruction 寄存器-立即数ALU:
ALUoutput←A op Imm
ADD R1, R2, #3
④ Branch 分支操作:
ALUoutput←NPC+Imm
Cond←(A op 0)
BEQZ R4, name

## Slide 55: 3.1 What is Pipelining----A Simple Implementation of DLX
4. Memory access/branch completion cycle (MEM):访存/分支操作完成
The only DLX instructions active in this cycle are loads, stores, and braches. 只有load、store和branch指令在这个周期活跃
① Memory reference: load and store 寄存器引用:
    LMD←Mem[ALUoutput] or
    Mem[ALUoutput]←B
② Branch 分支操作:
  if (Cond) PC←ALUoutput
  else PC←NPC

## Slide 56: 3.1 What is Pipelining----A Simple Implementation of DLX
5. Write-back cycle (WB) 写回:
① Register-Register ALU instruction
  Reg[IR16..20]←ALUoutput
② Register-Immediate ALU instruction
  Reg[IR11..15]←ALUoutput
③ Load instruction
  Reg[IR11..15]←LMD

## Slide 57: 3.1 What is Pipelining----A Simple Implementation of DLX
 Figure: shows how an instruction flows through the datapath.

## Slide 58: 3.1 What is Pipelining----A Simple Implementation of DLX
Thinking: the performance of the unpipelined DLX 该非流水线DLX的性能问题:
The performance:
Branch and store: 4 cycles; all other instructions: 5 cycles.
If branch frequency = 12%, store frequency = 5%,
then overall CPI = 17%  4+83%  5 = 4.83.
How Can we improve CPI?
Complete ALU instructions during MEM, since they are idle in MEM . ALU指令可在MEM完成
Assuming ALU instructions occupy 47%, then improvement lead to:
CPI = 17%  4 + 47%  4 + 36%  5 = 4.36
improvement = 4.83/4.36 = 1.1

## Slide 59: 3.1 What is Pipelining----A Simple Implementation of DLX
Thinking: the performance of the unpipelined DLX 该非流水线DLX的性能问题:
How about other improvements ?
any other attempts -> decrease the CPI -> but increase the clock cycle time (since need to put more activity into a clock cycle). 要降低CPI就会增加时钟周期时间
So, it is a trade-off:
  clock cycle time  CPI.
  requires a detailed analysis.

## Slide 60: 3.1 What is Pipelining----A Simple Implementation of DLX
Thinking: the performance of the unpipelined DLX 该非流水线DLX的性能问题:
How about Long-cycle ?
Temporary registers can be deleted, since there not be any communication across clock cycles.
Every instruction would execute in one long clock cycle, writing the result into the data memory, registers, or PC at the end of the clock cycle.
    CPI =1.
    one long clock cycle  5 multicycle clock cycle
Why Designers would never use single-cycle?
Very inefficient, since different instruction has varied amount of work.
Requires duplication of functional units that can be shared in a multicycle implementation.

## Slide 61: 3.1 What is Pipelining----A Simple Implementation of DLX
Thinking: the performance of the unpipelined DLX 该非流水线DLX的性能问题:
Hardware is redundant:
Two ALUs:
  One to increment the PC, one for effective address and ALU computation
  They are not needed on the same clock cycle. So can merge by adding additional multiplexers and sharing the same ALU.

## Slide 62: 3.1 What is Pipelining----A Simple Implementation of DLX
 Figure: shows how an instruction flows through the datapath.

## Slide 63: 3.1 What is Pipelining----A Simple Implementation of DLX
Thinking: the performance of the unpipelined DLX 该非流水线DLX的性能问题:
Hardware is redundant:
Two ALUs:
  One to increment the PC, one for effective address and ALU computation
  They are not needed on the same clock cycle. So can merge by adding additional multiplexers and sharing the same ALU.
  Two memorys: 指令存储器和数据存储器
  Instructions and data could be stored in the same memory.
  Since the data and instruction accesses happen on different clock cycles.

## Slide 64: 3.1 What is Pipelining----A Simple Implementation of DLX
 Figure: shows how an instruction flows through the datapath.

## Slide 65: 3.2 The Basic Pipeline for DLX
How to pipeline ?
Almost no changes to non-pipeline DLX, just start a new instruction on each clock cycle. 只需在每个时钟周期开始一条新指令
The execution pattern is shown in the following figure, the typical way a pipeline structure is drawn.
  each instruction takes 5 clock cycles
  each clock cycle initiate a new instruction
  each cycle execute some part of five instructions.

## Slide 66: 3.2 The Basic Pipeline for DLX
Simple DLX pipeline: One each clock cycle, another instruction is fetched and begins its five-cycle execution.
Instruction number | Clock number |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Instruction i | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
  each instruction takes 5 clock cycles
  each clock cycle initiate a new instruction
  each cycle execute some part of five instructions.

## Slide 67
不要求会画
要求会画

## Slide 68: 3.2 The Basic Pipeline for DLX
The pipeline can be thought of as a series of datapaths shifted in time.

## Slide 69: 3.2 The Basic Pipeline for DLX
Overlapping the execution of multiple instructions introduces observations:
must assure: not to perform two different operations with the same datapath resource on the same clock cycle.
a ALU cannot at the same time do compute an effective address and perform a subtract operation.
The basic datapath already use separate instruction and data memories, which we would typically implement with separate instruction and data caches.
The register file is used in the two stages: for reading in ID and for writing in WB.
PC: The problem arises when we consider the effect of branches, which changes the PC also, but not until the MEM stage.

## Slide 70: 3.1 What is Pipelining----A Simple Implementation of DLX

## Slide 71: 3.2 The Basic Pipeline for DLX
在IF段完成PC计算

## Slide 72: 3.2 The Basic Pipeline for DLX
The real pipeline:
Requires that values passed from one pipe stage to the next must be placed in registers. 流水线段之间传送的值必须放在寄存器中
Following figure shows the DLX pipeline with the appropriate registers, called pipeline registers or pipeline latches, between pipeline stages. 流水线寄存器，或者叫流水线锁存器
The registers are labeled with the names of the stages they connect.

## Slide 73: 3.2 The Basic Pipeline for DLX
Figure: The datapath is pipelined by adding a set of registers, one between each pair of pipe stages.

## Slide 74: 3.2 The Basic Pipeline for DLX

## Slide 75: 3.2 The Basic Pipeline for DLX
The real pipeline:
The pipeline registers carry both data and control information. 流水线寄存器包含数据和控制信息
Any value must be placed in a register and copied to next, until no longer needed. Otherwise, values could be overwritten before all used were completed.值放在寄存器中, 沿流水线传送, 直至不再需要

## Slide 76: 3.2 The Basic Pipeline for DLX

## Slide 77: 3.2 The Basic Pipeline for DLX

## Slide 78: 3.2 The Basic Pipeline for DLX
The real pipeline:
Example: where to find the register operand used for write on a load or ALU operation in WB?
register operand used for write on a load or ALU operation is supplied from MEM/WB pipeline register rather than from IF/ID register. load或ALU要写的寄存器由MEM/WB流水线寄存器提供
Reason: we want to write the register designated by that operation, not the register field of the instruction currently transitioning from IF to ID!

## Slide 79: 3.2 The Basic Pipeline for DLX
Events on every pipes stage of the DLX pipeline:
Any instruction is active in exactly one stage of the pipeline at a time, therefore any actions taken on behalf of an instruction occur between a pair of pipeline registers.
We can look at activities of the pipeline by examining what has to happen on any pipeline stage depending on the instruction type.

## Slide 80: 3.2 The Basic Pipeline for DLX
Figure: Events on every pipes stage of the DLX pipeline
Stage
Any instruction
IF
ID
IF/ID.IR ← Mem[PC]
IF/ID.NPC, PC ← (if EX/MEM.cond{EX/MEM.ALUOutput} else {PC+4});
ID/EX.A ← Regs[IF/ID.IR6...10]; ID/EX.B ← Regs[IF/ID.IR11...15];
ID/EX.NPC ← IF/ID.NPC; ID/EX.IR ← IF/ID.IR;
ID/EX.Imm ← (IF/ID.IR16)16##IF/ID.IR16...31;
In IF, fetch instruction, compute new PC, store incremented PC both into PC and pipeline register (NPC) for later use.
In ID, fetch registers, extend sign of lower 16 bits of IR, and pass along IR and NPC.

## Slide 81: 3.2 The Basic Pipeline for DLX

## Slide 82: 3.2 The Basic Pipeline for DLX
Figure: Events on every pipes stage of the DLX pipeline
During EX, perform ALU operation or address calculation; pass along IR and B register (if the instruction is store). Also set the value of cond to 1 if the instruction is a taken branch.
ALU instruction
Load/Store instruction
Branch instruction
EX
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A func ID/EX.B
(Register-Register) or EX/MEM.ALUOutput ← ID/EX.A op ID/EX.Imm;
(Register-Immediate)
EX/MEM.cond ← 0;
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A + ID/EX.Imm;
EX/MEM.cond ← 0;
EX/MEM.B ←ID/EX.B
EX/MEM.ALUOutput← ID/EX.NPC+ID/EX.Imm;
EX/MEM.cond ← (ID/EX.A op 0);

## Slide 83: 3.2 The Basic Pipeline for DLX

## Slide 84: 3.2 The Basic Pipeline for DLX
During MEM, cycle memory, write PC if needed, and pass along values needed in the final stage.
During WB, update the register field from either the ALU output or the loaded value.
MEM
WB
MEM/WB.IR ←EX/MEM.IR;
MEM/WB.ALUOutput ← EX/MEM.ALUOutput;
MEM/WB.IR ← EX/MEM.IR;
MEM/WB.LMD ← Mem[EX/MEM.ALUOutput]; or Mem[EX/MEM.ALUOutput] ← EX/MEM.B;
Regs[MEM/WB.IR16...20] ← MEM/WB.ALUOutput;
(Register-Register) or Regs[MEM/WB.IR11...15] ← MEM/WB.ALUOutput;
(Register-Immediate)
Regs[MEM/WB.IR11...15] ← MEM/WB.LMD;
ALU instruction
Load/Store instruction
Branch instruction

## Slide 85: Computer Architecture 计算机体系结构
School of Computer and Information Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 87
J-type (jump) instructions consist of just the opcode and a 26-bit operand, which is used to calculate the destination address.

## Slide 88: 3.2 The Basic Pipeline for DLX
Simple DLX pipeline: One each clock cycle, another instruction is fetched and begins its five-cycle execution.
Instruction number | Clock number |  |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
Instruction i | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
  each instruction takes 5 clock cycles
  each clock cycle initiate a new instruction
  each cycle execute some part of five instructions.

## Slide 89: 3.1 What is Pipelining----A Simple Implementation of DLX

## Slide 90: 3.2 The Basic Pipeline for DLX
在IF段完成PC计算

## Slide 91: 3.2 The Basic Pipeline for DLX

## Slide 92: 3.2 The Basic Pipeline for DLX
Figure: Events on every pipes stage of the DLX pipeline
Stage
Any instruction
IF
ID
IF/ID.IR ← Mem[PC]
IF/ID.NPC, PC ← (if EX/MEM.cond{EX/MEM.ALUOutput} else {PC+4});
ID/EX.A ← Regs[IF/ID.IR6...10]; ID/EX.B ← Regs[IF/ID.IR11...15];
ID/EX.NPC ← IF/ID.NPC; ID/EX.IR ← IF/ID.IR;
ID/EX.Imm ← (IF/ID.IR16)16##IF/ID.IR16...31;
In IF, fetch instruction, compute new PC, store incremented PC both into PC and pipeline register (NPC) for later use.
In ID, fetch registers, extend sign of lower 16 bits of IR, and pass along IR and NPC.

## Slide 93: 3.2 The Basic Pipeline for DLX
Figure: Events on every pipes stage of the DLX pipeline
During EX, perform ALU operation or address calculation; pass along IR and B register (if the instruction is store). Also set the value of cond to 1 if the instruction is a taken branch.
ALU instruction
Load/Store instruction
Branch instruction
EX
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A func ID/EX.B
(Register-Register) or EX/MEM.ALUOutput ← ID/EX.A op ID/EX.Imm;
(Register-Immediate)
EX/MEM.cond ← 0;
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A + ID/EX.Imm;
EX/MEM.cond ← 0;
EX/MEM.B ←ID/EX.B
EX/MEM.ALUOutput← ID/EX.NPC+ID/EX.Imm;
EX/MEM.cond ← (ID/EX.A op 0);

## Slide 94: 3.2 The Basic Pipeline for DLX
During MEM, cycle memory, write PC if needed, and pass along values needed in the final stage.
During WB, update the register field from either the ALU output or the loaded value.
MEM
WB
MEM/WB.IR ←EX/MEM.IR;
MEM/WB.ALUOutput ← EX/MEM.ALUOutput;
MEM/WB.IR ← EX/MEM.IR;
MEM/WB.LMD ← Mem[EX/MEM.ALUOutput]; or Mem[EX/MEM.ALUOutput] ← EX/MEM.B;
Regs[MEM/WB.IR16...20] ← MEM/WB.ALUOutput;
(Register-Register) or Regs[MEM/WB.IR11...15] ← MEM/WB.ALUOutput;
(Register-Immediate)
Regs[MEM/WB.IR11...15] ← MEM/WB.LMD;
ALU instruction
Load/Store instruction
Branch instruction

## Slide 95: 3.2 The Basic Pipeline for DLX
如何控制流水线？4个多路选择器:
Multiplexer in IF chooses whether to use value of incremented PC or of EX/MEM.ALUOutput (target) to write into the PC, controlled by EX/MEM.cond. IF段的MUX由EX/MEM.Cond域的值控制
Two multiplexers in ALU are set depending on instruction type, dictated by ID/EX.IR register. ALU输入端的MUX由ID/EX.IR所指出的指令类型控制
top multiplexer: whether instruction is branch.
bottom multiplexer: whether instruction is a R-R operation or other type of operation.
Fourth multiplexer: whether the instruction in WB is a load or a ALU operation. WB段的MUX由当前指令类型(Load/ALU)控制

## Slide 96: 3.2 The Basic Pipeline for DLX
如何控制流水线？4个多路选择器:

## Slide 97: 3.2 The Basic Pipeline for DLX
流水线改进的是吞吐量：
Pipelining increases instruction throughput, but does not reduce time of one instruction. 增加了吞吐量, 但没有降低每条指令的运行时间
It usually slightly increases execution time of each instruction due to overhead in control. 由于控制开销, 每条指令运行时间稍微增加
throughput increase -> program runs faster. 吞吐量增加，程序运行更快
Basic Performance Issues in Pipelining
流水线的基本性能问题

## Slide 98: 3.2 The Basic Pipeline for DLX
加速比：
假设为m段流水线，共n个任务，则加速比为？

## Slide 99: 3.2 The Basic Pipeline for DLX
影响流水线性能的因素：
In addition to limitations arising from pipeline latency, limits arise from imbalance among pipe stages and from pipelining overhead.
Imbalance: clock can run no faster than the time needed for the slowest pipeline stage.
Overhead: arises from combination of pipeline register delay and clock skew. 流水线开销，寄存器延迟和时钟偏差
  Register setup time: input must be stable before clock signal, plus propagation delay.
  Clock skew: max delay between two registers.

## Slide 100: 3.2 The Basic Pipeline for DLX
Example: Consider the unpipelined machine early.
Assume:
clock: 10ns;
ALU: 4 cycles, 40%;
branches: 4 cycles, 20%;
memory operations: 5 cycles, 40%.
Suppose: due to skew and setup, pipelining machine adds to clock overhead =1ns.
Ignore any latency impact, how much speedup we will gain from pipeline ?

## Slide 101: 3.2 The Basic Pipeline for DLX
Answer: The average instruction execution time on the unpipelined machine is:
In pipelined machine, clock must run at the speed of slowest stage plus overhead:
10 + 1 = 11 ns;
This is the average instruction execution time.

## Slide 102: 3.2 The Basic Pipeline for DLX
Answer:
Thus, the speedup from pipelining is:
The 1ns overhead essentially establishes a limit on the effectiveness of pipelining.

## Slide 103: 3.2 The Basic Pipeline for DLX
Example: Assume that the times required for the 5 functional units (5 cycles), are: 10 ns, 8 ns, 10 ns, 10 ns, 7ns.
Assume: pipelining adds 1ns of overhead.
Find speedup versus single-cycle datapath.
Answer:
unpipelined machine -> executes all instructions in one clock cycle -> average time per instruction is simply the clock cycle time.
clock time is sum of the times for each step:
Average instruction execution time
= 10+8+10+10+7 = 45ns

## Slide 104: 3.2 The Basic Pipeline for DLX
Answer:
pipelined machine -> clock time must be largest time for any stage (10ns) + overhead (1ns) = 11ns.
CPI =1, average execution time=11 ns. Thus:

## Slide 105: 3.2 The Basic Pipeline for DLX
有关流水线性能的若干问题
流水线并不能减少（而且一般是增加）单条指令的执行时间，但能够提高吞吐率
增加流水线的深度可以提高流水线性能
流水线深度受限于流水线的延迟和额外开销
需要用高速锁存器作为流水线寄存器
指令之间存在的相关，限制了流水线的性能

## Slide 106: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Hazards: situations that prevent the next instruction from executing. Hazards reduce performance from the ideal speedup gained by pipelining. 流水线中的相关是指相邻或相近的两条指令因存在某种关联，后一条指令不能在原先指定的时钟周期开始执行。
There are three classes of hazards:
Structural hazards: are resource conflicts, hardware cannot support all possible combinations of instructions in overlapped execution. 结构相关
Data hazards: an instruction depends on the results of a previous instruction. 数据相关
Control hazards: arise from the pipelining of branches and other instructions that change PC. 控制相关

## Slide 107: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
  结构相关：当指令在重叠执行过程中，硬件资源满足不了指令重叠执行的要求，发生资源冲突时产生“结构相关”。
  数据相关：因一条指令需要用到前面指令的结果，而无法与产生结果的指令重叠执行时，就发生了数据相关。
  控制相关：当流水线遇到分支指令和其它会改变PC值的指令时就发生控制相关。
  Hazards in pipelines can make it necessary to stall the pipeline (暂停流水线)
  Assume: when an instruction is stalled. All instructions issued later than the stalled instruction are also stalled. Instructions issued earlier than the stalled instruction must continue. No new instructions are fetched during stall.

## Slide 108: 3.2 The Major Hurdle of Pipelining–Pipeline Hazards
Stalls degrade pipeline performance. Simple equation for finding speedup :
Performance of Pipeline with Stalls
带暂停流水线的性能

## Slide 109: 3.2 The Major Hurdle of Pipelining–Pipeline Hazards
Assume 1: That pipelining can be thought of as decreasing the CPI:
Ideal CPI on pipelined machine is always 1, So
CPI pipelined:
If ignore overhead of pipelining and assume perfectly balanced, then cycle time of two machines can be equal, thus:

## Slide 110: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
In this case, unpipelined CPI is equal to the depth of pipeline, leading to:
If there are no pipeline stalls, then leads to intuitive result: improvement is the depth. 若无流水线阻塞，则流水线改进正是流水线深度

## Slide 111: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Assume 2: That pipelining can be thought of as decreasing the clock cycle time:
Ideal CPI of both unpipeline and pipeline machine is 1
If perfectly balanced and no overhead, then:
Speedup from pipelining:
Thus, if there are no stalls, speedup is equal to pipeline depth. 若无阻塞，加速比是流水线深度

## Slide 112: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Structural Hazards: If some combination of instructions can not be accommodated because of resource conflicts (资源冲突), the machine is said to have a structural hazard:
The most common instances: Some functional unit is not fully pipelined. Then a sequence of instructions cannot proceed at the rate of one per clock cycle. 功能部件不是全流水
Another common way: some resource has not been duplicated enough to allow all combinations of instructions in the pipeline to execute.重复设置的资源数量不足
Structural Hazards 结构冒险

## Slide 113: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Structural Hazards: Figure: a machine with one memory port will generate a conflict when a memory reference occurs.
the load instruction uses the memory for a data access at the same time instruction 3 wants to fetch an instruction from memory.

## Slide 114: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
To resolve, stall the pipeline for one clock cycle when the data memory access occurs.

## Slide 115: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
The figure shows pipeline datapath with the stall cycle added.
The effect is no instruction finish during clock 8, when instruction 3 would normally have finished.
Instruction 1 is assumed to not be load or store; otherwise, instruction 3 cannot start execution.
Stall is commonly called pipeline bubble or just bubble, since it floats through the pipeline taking space but carrying no useful work.

## Slide 116: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Rather than draw pipeline datapath, designers often just indicate stall behavior using a simpler diagram with only stage names.
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
load instruction | IF | ID | EX | MEM | WB |  |  |  |  | 
instruction i+1 |  | IF | ID | EX | MEM | WB |  |  |  | 
instruction i+2 |  |  | IF | ID | EX | MEM | WB |  |  | 
instruction i+3 |  |  |  | stall | IF | ID | EX | MEM | WB | 
instruction i+4 |  |  |  |  |  | IF | ID | EX | MEM | WB
instruction i+5 |  |  |  |  |  |  | IF | ID | EX | MEM
instruction i+6 |  |  |  |  |  |  |  | IF | ID | EX

## Slide 117: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Example: how much load structural hazard might cost.
Suppose:
  data references: 40%;
  ideal CPI : 1.
Assume: clock rate with structural hazard is 1.05 times higher than without hazard.
Is the pipeline with or without structural hazard faster, and by how much?

## Slide 118: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Answer:
Compute the average instruction time:
Ideal machine: no stalls, average instruction time is simply ：
Average instruction time with structural hazard:

## Slide 119: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Answer:
Average instruction time with structural hazard:
Machine without the hazard is 1.3 times faster.
Solution(加硬件): provide a separate memory access for instructions, either:
Split cache into instruction and data caches.
Use instruction buffers, to hold instructions.

## Slide 120: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Example:当前许多机器都没有将浮点功能单元完全流水，比如在DLX实现中，浮点乘需要5个时钟周期， 但对该指令不流水。请分析由此引起的结构相关。对某基准程序在DLX上运行的性能有何影响？假设基准程序中浮点乘法出现的频率约为14%。
最坏情况：每个浮点乘都无法与其它操作重叠执行，都需要5个周期，此时CPI为1.56 。
最好情况：可以完全重叠执行，仅需要1个周期，此时没有性能损失。

## Slide 121: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
A designer allow structural hazards, because:
Two reasons: (1) reduce cost. (2) reduce the latency of the unit.
(1) Pipelining all functional units, or duplicating them, may be too costly.
(2) Shorter latency (not fully pipelined) : comes from lack of pipeline registers that introduce overhead.
Data hazards cause pipeline to stall, preventing structural hazards from initiated.

## Slide 122: 3.4 Data Hazards
Consider the pipelined execution of the instructions:
  ADD R1， R2，R3
  SUB R4， R1，R5
  AND R6， R1，R7
  OR R8， R1，R9
  XOR R10，R1，R11
当指令在流水线中重叠执行时，流水线有可能改变指令读/写操作数的顺序，使之不同于它们在非流水实现时的顺序，这将导致数据相关
Data hazards: occur when pipeline changes the order of read/write accesses to operands, so that the order differs from the older seen by sequentially executing instructions on an unpipelined machine.

## Slide 123: 3.4 Data Hazards
Figure: The use of the result of the ADD instruction in the next three instructions causes a hazard.

## Slide 124: 3.4 Data Hazards
All instructions after ADD use ADD’s result.
ADD instruction writes value of R1 in WB, but SUB reads value in its ID. If not careful, SUB will read wrong value.
AND also affected. write R1 doesn’t complete until end of clock 5. AND reads registers during clock 4, will receive wrong results.
XOR operates properly, because its register read occurs in clock 6, after register write.
OR can be made to operate without hazard by implementation technique: reads register in second half cycle, writes in first half cycle.
  ADD R1， R2，R3
  SUB R4， R1，R5
  AND R6， R1，R7
  OR R8， R1，R9
  XOR R10，R1，R11

## Slide 125: 3.4 Data Hazards
Forwarding定向: also called bypassing or short-circuiting.
Forwarding works as follows:
ALU result from EX/MEM register is always fed back to ALU input latches.
If the forwarding hardware detects previous ALU has written a pipeline register, it is a source for current ALU, control logic select forwarded result (not register file) as input.
Minimizing Data Hazard Stalls By Forwarding
通过前送最小化数据冒险造成的停顿

## Slide 126: 3.4 Data Hazards
Figure: shows example with bypass paths and highlighting register read and writes.

## Slide 127: 3.4 Data Hazards
Figure: if AND R6， R1，R7 changed into AND R6， R1， R4
R4

## Slide 128: 3.4 Data Hazards
Forwarding定向: also called bypassing or short-circuiting.
主要思路：将计算结果从其产生的地方直接送到真正需要它的地方，就可以避免暂停。
  寄存器文件EX/MEM中的ALU运算结果总是回送到ALU的输入寄存器
  从定向通路得到输入数据的ALU操作不必从源寄存器中读取操作数

## Slide 129: 3.4 Data Hazards
Forwarding can be generalized to include passing a result directly to the functional unit that requires it: A result is forwarded from one unit to the input of another unit (DM, ALU), rather than just from the result of a unit to the input of the same unit (ALU, ALU).
一个结果不仅可以从某一功能单元的输出定向到其自身的输入，而且还可以定向到其它功能单元的输入
Example:
ADD R1, R2, R3
LW R4, 0(R1)
SW 12(R1), R4
Need to forward R1 and R4 from pipeline registers to ALU and data memory inputs.

## Slide 130: 3.4 Data Hazards
Figure: stores require an operand during MEM, and forwarding of that operand is shown here.
Result of load is forwarded from memory output in MEM/WB to the memory input to be stored.
ALU output is forwarded to ALU input for address calculation of both the load and the store.

## Slide 131: Computer Architecture 计算机体系结构
School of Computer and Information Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 132: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
Structural Hazards: If some combination of instructions can not be accommodated because of resource conflicts (资源冲突)， the machine is said to have a structural hazard:
The most common instances: Some functional unit is not fully pipelined. Then a sequence of instructions cannot proceed at the rate of one per clock cycle. 功能部件不是全流水
Another common way: some resource has not been duplicated enough to allow all combinations of instructions in the pipeline to execute.重复设置的资源数量不足
Structural Hazards 结构冒险

## Slide 133: 3.3 The Major Hurdle of Pipelining–Pipeline Hazards
A designer allow structural hazards, because:
Two reasons: (1) reduce cost. (2) reduce the latency of the unit.
(1) Pipelining all functional units, or duplicating them, may be too costly.
(2) Shorter latency (not fully pipelined) : comes from lack of pipeline registers that introduce overhead.
Data hazards cause pipeline to stall, preventing structural hazards from initiated.

## Slide 134: 3.4 Data Hazards
当指令在流水线中重叠执行时，流水线有可能改变指令读/写操作数的顺序，使之不同于它们在非流水实现时的顺序，这将导致数据相关
Data hazards: occur when pipeline changes the order of read/write accesses to operands, so that the order differs from the older seen by sequentially executing instructions on an unpipelined machine.
Consider two instructions i and j, with i occurring before j. The possible data hazards are: RAW, WAW, WAR.
RAW (read after write) 先写后读
WAW (write after write) 写后再写
WAR (write after read) 先读后写
RAR (read after read ) is not a hazard

## Slide 135: 3.4 Data Hazards
Forwarding定向: also called bypassing or short-circuiting.
主要思路：将计算结果从其产生的地方直接送到真正需要它的地方，就可以避免暂停。
  寄存器文件EX/MEM中的ALU运算结果总是回送到ALU的输入寄存器
  从定向通路得到输入数据的ALU操作不必从源寄存器中读取操作数

## Slide 136: 3.4 Data Hazards
Figure: if AND R6， R1，R7 changed into AND R6， R1， R4
R4

## Slide 137: 3.4 Data Hazards
Data hazards may be classified as three types, depending on order of read and write accesses.
Consider two instructions i and j, with i occurring before j. The possible data hazards are: RAW, WAW, WAR.
RAW (read after write) 先写后读
WAW (write after write) 写后再写
WAR (write after read) 先读后写
RAR (read after read ) is not a hazard
Data Hazard Classification
数据相关分类

## Slide 138: 3.4 Data Hazards
① RAW (read after write) 先写后读：j tries to read a source before i writes it, so j incorrectly gets the old value. 如果j 在i 完成写之前从R 中读出数据，将得到错误的结果
the most common type of hazard. 最常见的数据相关，严重制约了CPU的性能，是程序最重要的特征之一
the kind that we use forwarding to overcome

## Slide 139: 3.4 Data Hazards
② WAW (write after write) 写后再写： j tries to write an operand before it is written by i. 如果j 在i 之前完成写操作，R中将保存错误的结果
Present only in pipelines that write in more than one stage, or previous stalled, current continue.
The DLX integer pipeline writes a register only in WB and avoids this class of hazards.
If we made two changes to the DLX pipeline, WAW hazards would be possible.
First, move write back for ALU operation into MEM stage.
Second, suppose that the data memory access took two pipe stages.

## Slide 140: 3.4 Data Hazards
② WAW (write after write) 写后再写
The execution will leave the result of the first write (LW) in R1, rather than the result of ADD!
LW R1, 0(R2) | IF | ID | EX | MEM1 | MEM2 | WB
ADD R1, R2, R3 |  | IF | ID | EX | WB | 
先写
后写

## Slide 141: 3.4 Data Hazards
③ WAR (write after read)先读后写：j tries to write a destination before it is read by i. 如果j 先将数据写入R，i 将读出错误的结果
Cannot happen in our example pipeline because all reads are early (ID) and all writes are late (WB).
Natural structure of pipeline -> typically reads before it writes results -> such hazards are rare.
Modify pipeline as above, also read source for a store instruction, WAR hazard could occur.

## Slide 142: 3.4 Data Hazards
③ WAR (write after read)先读后写
SW 0(R1), R2 | IF | ID | EX | MEM1 | MEM2 | WB
ADD R2, R3, R4 |  | IF | ID | EX | WB | 
前半周期写
后半周期读
If SW reads R2 during second half of its MEM2 and ADD writes R2 during first half of its WB, SW will incorrectly read the value produced by ADD.
如果在这个阶段读R2.
DLX不是这样.

## Slide 143: 3.4 Data Hazards
Not all potential data hazards can be handled by bypassing.并非所有数据相关都可以通过定向技术解决。
Consider following sequence:
Data Hazards Requiring Stalls
需要停顿的数据冒险
LW R1，0（R2）
SUB R4，R1，R5
AND R6，R1，R7
OR R8，R1，R9

## Slide 144: 3.4 Data Hazards
Figure: The load instruction can bypass its result to the AND and OR instruction, but not to SUB.

## Slide 145: 3.4 Data Hazards
Pipeline interlock: add hardware, to preserve correct execution. It detects a hazard and stalls pipeline until hazard is cleared.
增加流水线“流水线互锁”部件，当互锁硬件发现这种相关后，就暂停流水线，直到相关消除。
The pipe interlock introduces a stall or bubble.
CPI increases by the length of the stall. CPI的增加就是阻塞的大小

## Slide 146: 3.4 Data Hazards
Pipeline interlock: add hardware, to preserve correct execution. It detects a hazard and stalls pipeline until hazard is cleared.
增加流水线“流水线互锁”部件，当互锁硬件发现这种相关后，就暂停流水线，直到相关消除。

## Slide 147: 3.4 Data Hazards
Figure: In top half, we can see why a stall is needed. This problem is solved by inserting a stall, as shown in the bottom half.

## Slide 148: 3.4 Data Hazards
Example:
Suppose:
  30% of instructions are loads.
  half time the instruction following a load depends on the result of load.
  This hazard creates a 1-cycle delay.
  How faster is the ideal pipelined machine (CPI =1) than the real pipeline ( with load stall) ?
  Answer:
  CPI = (1-0.3)  1 + (0.3  0. 5 1) + (0.3  0. 5 2) = 1.15.
  So the ideal machine is 1.15 times faster.

## Slide 149: 3.4 Data Hazards
Instruction issue: ID->EX: process of letting an instruction move from ID into EX.
For DLX integer pipeline, all data hazards can be checked during ID phase. 对DLX整数流水线, 所有冒险都可在ID阶段检测出来
If a data hazard exists, the instruction is stalled before it is issued. 如果有冒险, 就在发射之前停顿
Likewise, we determine what forwarding will be needed during ID and set appropriate controls then. 在ID阶段还确定需要的前送,并在需要时施加相应的控制
Implementing Control for DLX Pipeline
实现对DLX流水线的控制

## Slide 150: 3.4 Data Hazards
Method 1: detecting interlocks early -> never has to suspend instruction (unless entire is stalled) -> reduces hardware complexity.
Method 2: detect hazard or forwarding at start of a clock that uses operand (EX and MEM for this pipeline).

## Slide 151: 3.4 Data Hazards
Figure: lists the variety of circumstances that we must handle.
Situation | Example code sequence
No dependence | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R6, R7 OR R9, R6, R7
Dependence requiring stall | LW R1, 45(R2) ADD R5, R1, R7 SUB R8, R6, R7 OR R9, R6, R7
Dependence overcome by forwarding | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R1, R7 OR R9, R6, R7
Dependence with access in order | LW R1, 45(R2) ADD R5, R6, R7 SUB R8, R6, R7 OR R9, R1, R7

## Slide 152: 3.4 Data Hazards
Load interlock---LOAD instruction: Load互锁的检测与实现
Figure: detects all load interlocks when the instruction using load result is in ID. 当用到load结果的指令处于ID时检测所有的load互锁
Opcode field of ID/EX (ID/EX.IR0..5) | Opcode field of IF/ID (IF/ID.IR0..5) | Matching operand fields
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR6..10
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR11..15
Load | Load, store, ALU immediate, or branch | ID/EX.IR11..15=IF/ID.IR6..10

## Slide 153: 3.4 Data Hazards
Opcode field of ID/EX (ID/EX.IR0..5) | Opcode field of IF/ID (IF/ID.IR0..5) | Matching operand fields
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR6..10
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR11..15
Load | Load, store, ALU immediate, or branch | ID/EX.IR11..15=IF/ID.IR6..10
Format | Bits |  |  |  |  | 
 | 0 5 | 6 10 | 11 15 | 16 20 | 25 | 26 31
R-type | 0x0 | Rs1 | Rs2 | Rd | unused | func
I-type | opcode | Rs1 | Rd | immediate |  | 
J-type | opcode | offset added to PC |  |  |  | 

## Slide 154: 3.4 Data Hazards
Load interlock---LOAD instruction:

## Slide 155: 3.4 Data Hazards
Forwarding---mainly ALU instruction:
Pipeline registers contain both the data to be forwarded as well as the source and destination register fields. 前送的数据、源寄存器域、目的寄存器域都在流水线寄存器中
All forwarding logically happens:
from: ALU or data memory output
to: ALU input, data memory input, or zero detection unit.
Forwarding is by comparison:
Destination registers目标寄存器 of IR in EX/MEM and MEM/WB
Source registers 源寄存器 of IR in ID/EX and EX/MEM.
是否相同？

## Slide 156: 3.4 Data Hazards

## Slide 157: 3.4 Data Hazards
Following figure shows the comparisons and possible forwarding operations where the destination of the forwarded result is an ALU input for the instruction currently in EX.
In additional to the comparators and combinational logical that we need to determine when a forwarding path needs to be enabled, we also need to enlarge the multiplexers at the ALU inputs and add the connections from the pipeline registers that are used to forwarding the results.

## Slide 158: 3.4 Data Hazards
ADD R1, R2, R3 IF ID EX ME WB
SUB R5, R1, R7 IF ID EX ME WB
XOR R6, R1, R7 IF ID EX ME WB
OR R7, R1, R7 IF ID EX ME WB

## Slide 159: 3.4 Data Hazards

## Slide 160: 3.4 Data Hazards
ADDI R1, R2, #3 IF ID EX ME WB
SUB R5, R1, R7 IF ID EX ME WB
XOR R6, R1, R7 IF ID EX ME WB
OR R7, R1, R7 IF ID EX ME WB

## Slide 162: 3.4 Data Hazards
LW R1, 45(R2) IF ID EX ME WB
SUB R8, R6, R7 IF ID EX ME WB
ADD R5, R1, R7 IF ID EX ME WB

## Slide 164: 3.4 Data Hazards
ADD R1, R2, R3 IF ID EX ME WB
SW 0(R4), R1 IF ID EX ME WB
LW R1, 0(R2) IF ID EX ME WB
SW 0(R4), R1 IF ID EX ME WB

## Slide 165
LW R1, 56(R2) IF ID EX ME WB
SW R1, 45(R3) IF ID EX ME WB
SW R1, 45(R4) IF ID EX ME WB

## Slide 166: 3.4 Data Hazards
Forwarding of results to the ALU requires the addition of three extra inputs on each ALU multiplexer and the addition of three paths to the new inputs.

## Slide 167: Computer Architecture 计算机体系结构
School of Computer and Information Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 168: 3.4 Data Hazards
Load interlock---LOAD instruction: Load互锁的检测与实现
Figure: detects all load interlocks when the instruction using load result is in ID. 当用到load结果的指令处于ID时检测所有的load互锁
Opcode field of ID/EX (ID/EX.IR0..5) | Opcode field of IF/ID (IF/ID.IR0..5) | Matching operand fields
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR6..10
Load | Register- register ALU | ID/EX.IR11..15=IF/ID.IR11..15
Load | Load, store, ALU immediate, or branch | ID/EX.IR11..15=IF/ID.IR6..10

## Slide 169: 3.4 Data Hazards
Forwarding---mainly ALU instruction:
Pipeline registers contain both the data to be forwarded as well as the source and destination register fields. 前送的数据、源寄存器域、目的寄存器域都在流水线寄存器中
All forwarding logically happens:
from: ALU or data memory output
to: ALU input, data memory input, or zero detection unit.
Forwarding is by comparison:
Destination registers目标寄存器 of IR in EX/MEM and MEM/WB
Source registers 源寄存器 of IR in ID/EX and EX/MEM.
是否相同？

## Slide 170: 3.4 Data Hazards

## Slide 171: 3.4 Data Hazards

## Slide 174: 3.4 Data Hazards
流水线中常常会遇到多种类型的暂停.
Example: The DLX code sequence for A = B + C
Compiler Scheduling for Data Hazards
数据冒险的编译调度
ADD must be stalled to allow the load of C to complete.
SW need not delayed further: forwarding passes result from MEM/WB to data memory.

## Slide 175: 3.4 Data Hazards
Pipeline scheduling or instruction scheduling
Rearrange code sequence to eliminate hazard, avoiding stalls. 编译器可以通过重新排列代码的顺序来消除这种暂停，这种技术就是“流水线调度”或“指令调度”
For example, avoid generating code with: a load followed by the immediate use of load destination register. 避免出现：load紧后面的指令需要load的结果

## Slide 176: 3.4 Data Hazards
Example: Generate DLX code that avoids pipeline stalls for the following sequence:
          a = b + c;
          d = e – f;
Assume loads have a latency of 1 clock cycle.
Answer:

## Slide 177: 3.4 Data Hazards
Both load interlocks (LW Rc, c to ADD Ra, Rb, Rc and LW Rf, f to SUB Rd, Re, Rf) are eliminated.
There is a dependence between ALU and store, but pipeline allows the result to be forwarded.
Notice: use different registers for first and second statements was critical for this schedule to be legal. If the variable e was loaded into the same register as b or c, this schedule would be illegal.
In general, pipeline scheduling can increase the register count required.

## Slide 178: 3.5 Control Hazards
Control hazards: arise from the pipelining of branches and other instructions that change PC.
Control hazards: can cause great performance loss for DLX pipeline than do data hazards. 可能比数据冒险造成的性能损失更大
If a branch changes the PC to its target address, it is a taken branch; if it fails, it is not taken, or untaken.
If is a branch taken, then PC is not changed until the end of MEM (address calculated). 转移如果成功, PC直到MEM结束(更新完地址)才改变
The simplest method is to stall pipeline upon detecting branch until it reach MEM, which determines new PC.一旦ID段检测到分支指令，就暂停执行其后的指令，直到分支指令达到Mem段，确定新的PC为止

## Slide 179: 3.5 Control Hazards

## Slide 180: 3.5 Control Hazards
Figure: A branch causes a 3-cycle stall
One cycle is a repeated IF cycle.
Two cycles are idle.
If branch is not taken, the second IF for branch successor is redundant.

## Slide 181: 3.5 Control Hazards
3 clock cycles is a significant loss.
With: branch frequency=30%, ideal CPI=1, then: 30%*(3+1)+70%*1= 1.9, only half ideal speedup.
The number of clock cycles in a branch stall can be reduced by two steps:
① Find out whether branch is taken or not earlier in the pipeline. 在流水线中尽早判断分支转移是否成功
② Compute the taken PC earlier (i.e. The address of the branch target). 转移成功时，尽早计算出转移目标地址
To optimize, both must be done. 同时采用，缺一不可

## Slide 182: 3.5 Control Hazards
In DLX:
the branch (BEQZ and BNEZ) require testing a register for equality to zero, it is possible to complete this decision by the end of the ID cycle by moving the zero test into the cycle. 将“=0?” 测试提前到ID段
Computing the branch target address during ID requires an additional adder. 在ID段增加一个加法器，计算分支目标地址
将分支判断结果和目标地址提前到ID/EX站前
With the separate adder and a branch decision made during ID, here is only a one-clock-cycle stall on branches.

## Slide 183: 3.5 Control Hazards

## Slide 184: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 185: 3.5 Control Hazards
Figure: The stall from branch hazards can be reduced by moving zero test and branch target calculation into ID.
We have made two important changes, each of which removes 1 cycle from the 3 cycle stall.
first change: move both branch address target calculation and branch condition decision to ID. 改变1: 将转移目标计算和转移条件测试挪到ID中
second change: write PC in IF, using either branch target address computed during ID or the incremented PC computed during IF. 改变2: 在IF写PC, 用ID阶段计算出的目标地址或者IF阶段计算出的递增PC. 数据一计算出来就能使用, 不用等到下一周期
In comparison, the origin pipeline obtains branch target address from EX/MEM register and wrote the result during MEM.

## Slide 186: 3.5 Control Hazards

## Slide 187: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 188: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 189: 3.5 Control Hazards
Branch instruction | IF | ID | EX | MEM | WB |  |  |  |  | 
Branch successor |  | IF | IF | ID | EX | MEM | WB |  |  | 
Branch successor+1 |  |  |  | IF | ID | EX | MEM | WB |  | 
Branch successor+2 |  |  |  |  | IF | ID | EX | MEM | WB | 
Branch successor+3 |  |  |  |  |  | IF | ID | EX | MEM | WB
Branch successor+4 |  |  |  |  |  |  | IF | ID | EX | MEM
Branch successor+5 |  |  |  |  |  |  |  | IF | ID | EX

## Slide 190: 3.5 Control Hazards
Stage
Any instruction
IF
ID
IF/ID.IR ← Mem[PC]
IF/ID.NPC, PC ← (if EX/MEM.cond{EX/MEM.ALUOutput} else {PC+4});
ID/EX.A ← Regs[IF/ID.IR6...10]; ID/EX.B ← Regs[IF/ID.IR11...15];
ID/EX.NPC ← IF/ID.NPC; ID/EX.IR ← IF/ID.IR;
ID/EX.Imm ← (IF/ID.IR16)16##IF/ID.IR16...31;
ALU instruction
Load/Store instruction
Branch instruction
EX
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A func ID/EX.B
(Register-Register) or EX/MEM.ALUOutput ← ID/EX.A op ID/EX.Imm;
(Register-Immediate)
EX/MEM.cond ← 0;
EX/MEM.IR ← ID/EX.IR;
EX/MEM.ALUOutput ← ID/EX.A + ID/EX.Imm;
EX/MEM.cond ← 0;
EX/MEM.B ←ID/EX.B
EX/MEM.ALUOutput← ID/EX.NPC+ID/EX.Imm;
EX/MEM.cond ← (ID/EX.A op 0);

## Slide 191: 3.5 Control Hazards
Figure: the branch portion of the revised pipeline table.
Pipe stage
Branch instruction
IF
ID
EX
IF/ID.IR ← Mem[PC];
IF/ID.NPC, PC ← (if ((IF/ID.opcode = = branch ) & (Regs[IF/ID.IR6...10 ] op 0)){IF/ID.NPC + (IF/ID. IR16 )16## IF/ID. IR16...31}else{PC+4})
ID/EX.A ← Regs[IF/ID. IR6...10]; ID/EX.B ← Regs[IF/ID.IR11...15]; ID/EX.IR ← IF/ID.IR;
ID/EX.Imm ← (IF/ID.IR16)16##IF/ID.IR16...31;
MEM
WB

## Slide 192: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 193: 3.5 Control Hazards
Figure: the branch portion of the revised pipeline table.
branch target address addition happens during ID, branch condition (Regs[IF/ID.IR6..10] op 0), both will be done for all instructions. 在ID阶段计算转移目标和转移条件
The selection of sequential PC or branch target PC still occurs during IF. 新PC的选择在IF
reduces branch penalty by two cycles: one from evaluating branch target and condition earlier, one from controlling PC selection on the same clock rather than on next clock. 改进2个周期: (1)更早计算转移地址和转移条件。(2) 在IF而不是下一个周期修改PC.
Since cond is set to 0, unless the instruction in ID is a taken branch, the machine must decode the instruction before the end of ID. 其它指令照例解码
Because branch is done by the end of ID, the EX, MEM, and WB stages are unused for branches. 转移在ID结束后就完成, EX、MEM、WB没有用到

## Slide 194: 3.5 Control Hazards
Figure: The figure reviews overall frequency of control flow operations for our SPEC subset on DLX.
Branch Behavior in Programs 程序中的转移行为

## Slide 195: 3.5 Control Hazards
The integer benchmarks show conditional branch frequencies of 14% to 16%, with much lower unconditional branch frequencies.
For FP benchmarks, the behavior is much more varied with a conditional branch frequency of 3% up to 12%, but overall average for both conditional branches and unconditional branches is lower than for the integer benchmarks.
Forward branches dominate backward branches by about 3.7 to 1 on average.

## Slide 196: 3.5 Control Hazards
Totaling 67% of the conditional branches are taken on average.
Combining two figures, 60% of the forward branches are taken on average and 85% of the backward branches are taken.
Figure: shows the frequency of forward and backward branches that are taken as a fraction of all conditional branches.

## Slide 197: 3.5 Control Hazards
Compile-time schemes: we discuss 4 simple compile-time schemes.
In these schemes, the actions for branch are static---they are fixed for each branch.
The software (compiler) can try to minimize branch penalty using knowledge of hardware scheme and of branch behavior.
Reducing Pipeline Branch Penalties
降低流水线中的转移造成的惩罚

## Slide 198: 3.5 Control Hazards
① freeze or flush the pipeline 冻结或排空流水线
The simplest scheme: freeze or flush the pipeline, holding or deleting any instructions after branch until branch destination is known.
思路：在流水线中停住或删除分支后的指令，直到知道转移目标地址
Advantages: simplicity both for hardware and software.

## Slide 199: 3.5 Control Hazards
② Treat branch as not taken 预测分支转移失败
A higher performance scheme: treat branch as not taken, allowing hardware to continue as if the branch were not executed.
Not to change machine state until the branch outcome is definitely known.
If branch is taken, we need to turn fetched instruction into a no-op (clearing IF/ID register) and restart fetch at the target address.
思路：流水线继续照常流动，如果分支转移成功，将分支指令后的指令转换为空操作，并从分支目标处开始取指令执行；否则照常执行

## Slide 200: 3.5 Control Hazards
② Treat branch as not taken 预测分支转移失败
branch instruction | IF | ID | EX | MEM | WB |  |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB |  | 
Branch target |  |  |  |  | IF | ID | EX | MEM | WB | 
Branch target+1 |  |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 201: 3.5 Control Hazards
② Treat branch as not taken 预测分支转移失败
Figure: shows situations of taken and untaken
Untaken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
Taken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | idle | idle | idle | idle |  |  | 
Branch target |  |  | IF | ID | EX | MEM | WB |  | 
Branch target+1 |  |  |  | IF | ID | EX | MEM | WB | 
Branch target+2 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 202: 3.5 Control Hazards
③ Treat branch as taken 预测分支转移成功
Upon branch decoded and target address computed, assume branch to be taken and begin fetching and executing at the target.
思路：始终假设分支成功，直接从分支目标处取指令执行
In DLX, we don’t know target address earlier than we know branch outcome, there is no advantage in this approach for DLX. DLX：知道转移目标地址不早于转移结果，所以对DLX流水线没有任何好处

## Slide 203: 3.5 Control Hazards
④ Delayed branch 延迟分支
In a delayed branch, the execution cycle with a branch delay of length n is:
branch instruction
sequential successor1
sequential successor2
........
sequential successorn
branch target if taken
延迟槽
转移指令
转移目标
思路：分支开销为n的分支指令后紧跟有n个延迟槽，流水线遇到分支指令时，按正常方式处理，顺带执行延迟槽中的指令，从而减少分支开销。
Branch-delay slots: These instructions are executed whether or not the branch is taken. 无论转移是否成功, 这些指令都被执行

## Slide 204: 3.5 Control Hazards
④ Delayed branch 延迟分支

## Slide 205: 3.5 Control Hazards
④ Delayed branch 延迟分支
Figure: Pipeline behavior of DLX pipeline, having one branch-delay slot.
Untaken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Branch-delay Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
Taken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Branch-delay Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Branch target |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+1 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+2 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 206: 3.5 Control Hazards
④ Delayed branch 延迟分支
The job of compiler is to make successor instructions valid and useful. 要求：使转移指令后面的指令(即延迟槽中的指令)正确且有用
Three ways branch delay can be scheduled.

## Slide 207: 3.5 Control Hazards
④ Delayed branch 延迟分支
From before:
Notake take
ADD ADD
If If
×× ×××
×××
Notake take
If If
ADD ADD
×× ×××
×××
××
×××
××
×××

## Slide 208: 3.5 Control Hazards
④ Delayed branch 延迟分支
From target:
××
××
Notake Take
SUB SUB
ADD ADD
if if
×× SUB
ADD
Notake Take
SUB SUB
ADD ADD
if if
SUB SUB
×× ADD

## Slide 209: 3.5 Control Hazards
④ Delayed branch 延迟分支
From fall through:
Notake Take
ADD ADD
If If
OR SUB
SUB
Notake Take
ADD ADD
If If
OR OR
SUB SUB

## Slide 210: 3.5 Control Hazards
④ Delayed branch 延迟分支
The different constraints for each of these branch-scheduling schemes, as well as situations in which they win.
Scheduling strategy | Requirements | Improves performance when?
From before 从前调度 | Branch must not depend on the rescheduled instructions. | Always
From target 从目标 处调度 | Must be ok to execute rescheduled instructions if branch is not taken. May need to duplicate instructions. | When branch is taken. May enlarge program if instructions are duplicated.
From fall through 从失败 处调度 | Must be ok to execute instructions if branch is taken. | When branch is not taken.

## Slide 211: Computer Architecture 计算机体系结构
School of Computer Science and Technology
Beijing Jiaotong Univeristy
Yi Tian

## Slide 212: 3.5 Control Hazards

## Slide 213: 3.5 Control Hazards
Figure: A branch causes a 3-cycle stall
One cycle is a repeated IF cycle.
Two cycles are idle.
If branch is not taken, the second IF for branch successor is redundant.

## Slide 214: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 215: 3.5 Control Hazards
Figure: revised pipelined datapath. Thus only a 1-clock-cycle stall on branches.

## Slide 216: 3.5 Control Hazards
Branch instruction | IF | ID | EX | MEM | WB |  |  |  |  | 
Branch successor |  | IF | IF | ID | EX | MEM | WB |  |  | 
Branch successor+1 |  |  |  | IF | ID | EX | MEM | WB |  | 
Branch successor+2 |  |  |  |  | IF | ID | EX | MEM | WB | 
Branch successor+3 |  |  |  |  |  | IF | ID | EX | MEM | WB
Branch successor+4 |  |  |  |  |  |  | IF | ID | EX | MEM
Branch successor+5 |  |  |  |  |  |  |  | IF | ID | EX

## Slide 217: 3.5 Control Hazards
① freeze or flush the pipeline 冻结或排空流水线
The simplest scheme: freeze or flush the pipeline, holding or deleting any instructions after branch until branch destination is known.
思路：在流水线中停住或删除分支后的指令，直到知道转移目标地址
Advantages: simplicity both for hardware and software.

## Slide 218: 3.5 Control Hazards
② Treat branch as not taken 预测分支转移失败
A higher performance scheme: treat branch as not taken, allowing hardware to continue as if the branch were not executed.
Not to change machine state until the branch outcome is definitely known.
If branch is taken, we need to turn fetched instruction into a no-op (clearing IF/ID register) and restart fetch at the target address.
思路：流水线继续照常流动，如果分支转移成功，将分支指令后的指令转换为空操作，并从分支目标处开始取指令执行；否则照常执行

## Slide 219: 3.5 Control Hazards
② Treat branch as not taken 预测分支转移失败
Figure: shows situations of taken and untaken
Untaken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
Taken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Instruction i+1 |  | IF | idle | idle | idle | idle |  |  | 
Branch target |  |  | IF | ID | EX | MEM | WB |  | 
Branch target+1 |  |  |  | IF | ID | EX | MEM | WB | 
Branch target+2 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 220: 3.5 Control Hazards
③ Treat branch as taken 预测分支转移成功
Upon branch decoded and target address computed, assume branch to be taken and begin fetching and executing at the target.
思路：始终假设分支成功，直接从分支目标处取指令执行
In DLX, we don’t know target address earlier than we know branch outcome, there is no advantage in this approach for DLX. DLX：知道转移目标地址不早于转移结果，所以对DLX流水线没有任何好处

## Slide 221: 3.5 Control Hazards
④ Delayed branch 延迟分支
In a delayed branch, the execution cycle with a branch delay of length n is:
branch instruction
sequential successor1
sequential successor2
........
sequential successorn
branch target if taken
延迟槽
转移指令
转移目标
思路：分支开销为n的分支指令后紧跟有n个延迟槽，流水线遇到分支指令时，按正常方式处理，顺带执行延迟槽中的指令，从而减少分支开销。
Branch-delay slots: These instructions are executed whether or not the branch is taken. 无论转移是否成功, 这些指令都被执行

## Slide 222: 3.5 Control Hazards
④ Delayed branch 延迟分支
The job of compiler is to make successor instructions valid and useful. 要求：使转移指令后面的指令(即延迟槽中的指令)正确且有用
Three ways branch delay can be scheduled.

## Slide 223: 3.5 Control Hazards
④ Delayed branch 延迟分支
The limitations on delayed-branch:
  Restrictions on the instructions that are scheduled into the delay slots.
  Ability to predict at compile time whether a branch is likely to be taken or not.
Advantage:
  Allowing the use of simple compiler scheduling to reduce branch penalties.

## Slide 224: 3.5 Control Hazards
④ Delayed branch 延迟分支
To improve the ability of the complier to fill branch delay slots, most machines with conditional branches have introduced a cancelling or nullifying branch (分支取消机制).
In a cancelling branch, the instruction includes the direction that the branch was predicted.
  When the branch behaves as predicted, the instruction in the branch-delay slot is simply executed as it would normally be with a delayed branch. 预测正确则照常执行
  When the branch is incorrectly predicted, the instruction in the branch-delay slot is simply turned into a no-op. 预测错误则取消

## Slide 225: 3.5 Control Hazards
④ Delayed branch 延迟分支
Figure: The behavior of a predicted-taken cancelling branch depends on whether the branch is taken or not.
Untaken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Branch-delay Instruction i+1 |  | IF | idle | idle | idle | idle |  |  | 
Instruction i+2 |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+3 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+4 |  |  |  |  | IF | ID | EX | MEM | WB
Taken branch instruction | IF | ID | EX | MEM | WB |  |  |  | 
Branch-delay Instruction i+1 |  | IF | ID | EX | MEM | WB |  |  | 
Branch target |  |  | IF | ID | EX | MEM | WB |  | 
Instruction i+1 |  |  |  | IF | ID | EX | MEM | WB | 
Instruction i+2 |  |  |  |  | IF | ID | EX | MEM | WB

## Slide 226: 3.5 Control Hazards
④ Delayed branch 延迟分支
The advantage of cancelling branches is that they eliminate the requirements on the instruction placed in the delay slot, enabling the compiler to use scheduling schemes ‘From target’ and ‘From fall through’ without meeting the requirements shown for these schemes in Figure 3.29.
In the early RISC machines with single-cycle branch delays, the delayed branch approach was attractive, since it yielded good performance with minimal hardware cost.
More recently, with deeper pipelines and longer branch delays, a delayed branch approach is less useful since it cannot easily hide the longer delays. With these longer branch delays, most architects have found it necessary to include more powerful hardware schemes for branch prediction.

## Slide 227: 3.5 Control Hazards
The effective pipeline speedup with branch penalties, assuming an ideal CPI of 1:
Performance of Branch Schemes
转移方案的性能

## Slide 228: 3.5 Control Hazards
Delayed branches are a technique that exposes a pipeline hazard so that the compiler can reduce the penalty associated with the hazard.
Effectiveness of delayed branches: depends on if we can correctly guess branch direction. Accurately predict a branch at compile time is also helpful scheduling data hazards.
Static Branch Prediction: Using Compiler Technology
静态转移预测：采用编译器技术
LW R1, 0(R2)
SUB R1, R1, R3
BEQZ R1, L
OR R4, R5, R6
ADD R10, R4, R3
L: ADD R7, R8, R9

## Slide 229: 3.5 Control Hazards
Delayed branches are a technique that exposes a pipeline hazard so that the compiler can reduce the penalty associated with the hazard.
Effectiveness of delayed branches: depends on if we can correctly guess branch direction
Accurately predict a branch at compile time is also helpful scheduling data hazards.
Two basic methods to statically predict branches:
(1) by examining program behavior.
(2) by using profile information collected from earlier runs of program.
Static Branch Prediction: Using Compiler Technology
静态转移预测：采用编译器技术

## Slide 230: 3.5 Control Hazards
Simplest scheme: predict a branch as taken
Another: predict on basis of branch direction, choosing:
backward-going branch -> taken
forward-going branches -> not taken.
More accurate technique: predict branches on the basis of profile information collected from earlier runs.
behavior of branches: often highly biased toward taken or untaken.
Static Branch Prediction: Using Compiler Technology
静态转移预测：采用编译器技术

## Slide 231: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
DLX floating-point operations: DLX FP operations complete in one cycle -> slow clock, or enormous logic in FP units -> impractical
DLX浮点操作在一个周期内完成不现实:多周期操作: 流水线中如何解决？
Imagine FP pipeline has two changes:
① EX may be repeat as many times as needed to complete the operation– the number of repetitions can vary for different operation.
② There may be multiple floating-point functional units.

## Slide 232: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Assume there four separate functional units in DLX implement:
① Integer unit: handles loads and stores, integer ALU operations, and branches. 整数单元
② FP and integer multiplier. 浮点和整数乘法器
③ FP adder: handles FP add, subtract, conversion. 浮点加法器
④ FP and integer divider. 浮点和整数除法器
Assume that the execution stages of these functional units are not pipelined.
Thus no instruction using a unit may issue until previous instruction leaves EX.
If an instruction cannot proceed to EX, the entire pipeline behind will be stalled.

## Slide 233: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: The DLX pipeline with three additional unpipelined, floating-point, functional units.
IF
ID
EX
Integer
unit
EX
FP/Integer
multiply
EX
FP adder
EX
FP/Integer
divide
MEM
WB

## Slide 234: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Latency: the number of intervening cycles between an instruction that produces a result and an instruction that uses the result. 从产生结果到能使用结果之间的周期数
Initiation interval or repeat interval: the number of cycles that must elapse between issuing two operations of a given type. 发射两个给定类型操作之间必须经过的周期数

## Slide 235: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: A pipeline that supports multiply outstanding FP operations.

## Slide 236: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Latency of integer unit 整数单元的Latency：
integer ALU: 0, since results can be used on next cycle. 结果在下一个周期就能用
load: 1, since results can be used after 1 cycle. 结果在过一个周期后才能用
store: 0 (对于被存的数)
Pipeline latency: equal to depth of EX pipeline - 1, the number of stages from EX to stage that produces result.
For above example, the number of stages:
FP add: 4, then latency=3
FP multiply: 7, then latency=6
achieve higher clock rate -> put fewer logic in each pipe stage -> number of pipe stages larger -> longer latency.
Thus, faster clock rate  longer latency.

## Slide 237: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: latencies and initiation intervals for functional units.
Functional unit | Latency | Initiation interval
Integer ALU | 0 | 1
Data memory (integer and FP loads) | 1 | 1
FP add | 3(4-1) | 1
FP multiply (also integer multiply) | 6(7-1) | 1
FP divide (also integer divide and FP sqrt) | 14(15-1) | 15

## Slide 238: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: A pipeline that supports multiply outstanding FP operations.

## Slide 239: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: A pipeline that supports multiply outstanding FP operations.
Repeat interval: by adding additional pipeline stages, separated by pipeline registers.
Requires additional pipeline registers (A1/A2, A2/A3, A3/A4), and ID/EX, ID/DIV, ID/M1, ID/A1.
Divide unit: take multiple cycles, are further subdivided to show the latency of those stages. Because they are not complete stages, only one operation may be active.

## Slide 240: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: A pipeline that supports multiply outstanding FP operations.
FP multiplier and adder are fully pipelined and have a depth of 7 and 4 stages.
FP divider, not pipelined, requires 15 cycles.
The latency between issue of an FP operation and the use of the result of that operation without incurring a RAW stall is determined by the number of cycles spent in the execution stages.
For example, the fourth instruction after an FP add can use the result of the FP add.
For integer ALU operations, the depth of the execution pipeline is always one and the next instruction can use the results.

## Slide 241: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: The pipeline timing of a set of independent FP operations.
MULTD | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB
ADDD |  | IF | ID | A1 | A2 | A3 | A4 | MEM | WB |  | 
LD |  |  | IF | ID | EX | MEM | WB |  |  |  | 
SD |  |  |  | IF | ID | EX | MEM | WB |  |  | 
 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
Need data
product data
The longer latency of the FP operations increases the frequency of RAW hazards and resultant stalls.

## Slide 242: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Aspects to hazard detection and forwarding for pipeline that supports multiple outstanding FP operations:
① Because the divide unit is not fully pipelined, structural hazards can occur. These will need to be detected and issuing instructions will need to be stalled. 除法单元未充分流水化, 可能导致结构冲突, 需要检测, 并使指令发射停顿
② Because the instructions have varying running times, the number of register writes required in a cycle can be larger than 1. Structural hazards: assume the FP register file has one write port. 指令运行时间不同, 会导致同一个周期有多个寄存器写操作, 形成结构冲突
Hazards and Forwarding in Longer Latency Pipelines
长延迟流水线的冒险和前送

## Slide 243: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: The pipeline timing of a set of independent FP operations.
MULTD | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB
ADDD |  | IF | ID | A1 | A2 | A3 | A4 | MEM | WB |  | 
LD |  |  | IF | ID | EX | MEM | WB |  |  |  | 
SD |  |  |  | IF | ID | EX | MEM | WB |  |  | 
 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
Need data
product data
The longer latency of the FP operations increases the frequency of RAW hazards and resultant stalls.

## Slide 244: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Aspects to hazard detection and forwarding for pipeline that supports multiple outstanding FP operations:
③ WAW hazards (Data hazard) are possible, since instruction no longer reach WB in order. Note that WAR hazards are not possible, since the register reads always occur in ID. 指令不再按序到达WB,可能导致WAW冒险。寄存器读总在ID发生,所以不会有WAR冒险。
④ Because of longer latency of operations, stalls for RAW hazards (Data hazard) will be more frequent. 操作的长延迟,导致RAW冲突更频繁。
Hazards and Forwarding in Longer Latency Pipelines
长延迟流水线的冒险和前送

## Slide 245: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: The pipeline timing of a set of independent FP operations.
MULTD | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB
ADDD |  | IF | ID | A1 | A2 | A3 | A4 | MEM | WB |  | 
LD |  |  | IF | ID | EX | MEM | WB |  |  |  | 
SD |  |  |  | IF | ID | EX | MEM | WB |  |  | 
 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
Need data
product data
The longer latency of the FP operations increases the frequency of RAW hazards and resultant stalls.

## Slide 246: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Structural hazards: Figure: the number of register writes required in a cycle can be larger than 1. The single register port represents a structural hazard.
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
MULTD F0, F4, F6 | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB
 |  | IF | ID | EX | MEM | WB |  |  |  |  | 
 |  |  | IF | ID | EX | MEM | WB |  |  |  | 
ADDD F2, F4, F6 |  |  |  | IF | ID | A1 | A2 | A3 | A4 | MEM | WB
 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
 |  |  |  |  |  | IF | ID | EX | MEM | WB | 
LD F8, 0(R2) |  |  |  |  |  |  | IF | ID | EX | MEM | WB
In cycle 11, all 3 instructions reach WB and want to write register file -> structural hazard. 在第11周期, 3条指令都到了WB阶段并要写寄存器文件, 从而导致结构冲突

## Slide 247: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Structural hazard: solutions.
With only 1 write port, machine must serialize the instruction. 若只有一个写端口, 就必须使指令串行化
Could increase write ports -> but unattractive since additional ports are used rarely. 可增加写端口数, 但没有吸引力, 因为增加的端口很少使用
Instead, we choose to detect and enforce access to write port as a structural hazard.

## Slide 248: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Deal with the hazard:
① track use of write port in ID and stall instruction before it issues. 早解决: 在ID阶段跟踪写端口的使用, 并在发射之前阻塞指令
If a instruction in ID needs to use register file at the same time as an instruction already issued, the instruction is stalled for a cycle. 如果检测到处于ID的指令与早先发射的指令在同一周期使用寄存器文件, 则该指令阻塞一个周期
Tracking is done by a shift register, each clock shifted one bit. 跟踪操作用移位寄存器实现, 每个周期移一位
Advantage: interlock detection and stall insertion occurs in the ID stage. 优点: 在ID阶段就完成互锁检测和阻塞插入
Cost: addition of shift register and write conflict logic. 成本: 要加入移位寄存器和写冲突逻辑

## Slide 249: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Deal with the hazard:
② stall a conflicting instruction when it tries to enter either MEM or WB. 到时候再解决: 在冲突指令要进入MEM或WB时阻塞之
Heuristic: give priority to the unit with longest latency, the one most likely to have caused another instruction to be stalled. 优先考虑具有最长潜伏期的指令, 这些指令最有可能引起其他指令阻塞
Advantage: not require detecting conflict until MEM or WB, so is easy to see. 优点: 到MEM或WB才检测冲突, 因此容易
Disadvantage: complicates pipeline control, as stalls can now arise from two places. 缺点: 使流水线控制复杂化, 因为可从两个地方插入阻塞

## Slide 250: Computer Architecture 计算机体系结构
School of Computer Science and Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 251: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure: A pipeline that supports multiply outstanding FP operations.

## Slide 252: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Aspects to hazard detection and forwarding for pipeline that supports multiple outstanding FP operations:
① Because the divide unit is not fully pipelined, structural hazards can occur. These will need to be detected and issuing instructions will need to be stalled. 除法单元未充分流水化, 可能导致结构冲突, 需要检测, 并使指令发射停顿
② Because the instructions have varying running times, the number of register writes required in a cycle can be larger than 1. Structural hazards: assume the FP register file has one write port. 指令运行时间不同, 会导致同一个周期有多个寄存器写操作, 形成结构冲突
Hazards and Forwarding in Longer Latency Pipelines
长延迟流水线的冒险和前送

## Slide 253: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Aspects to hazard detection and forwarding for pipeline that supports multiple outstanding FP operations:
③ WAW hazards (Data hazard) are possible, since instruction no longer reach WB in order. Note that WAR hazards are not possible, since the register reads always occur in ID. 指令不再按序到达WB,可能导致WAW冒险。寄存器读总在ID发生,所以不会有WAR冒险。
④ Because of longer latency of operations, stalls for RAW hazards (Data hazard) will be more frequent. 操作的长延迟,导致RAW冲突更频繁。
Hazards and Forwarding in Longer Latency Pipelines
长延迟流水线的冒险和前送

## Slide 254: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
RAW hazards: Figure: typical FP code sequence showing the stalls arising from RAW hazards.
Longer pipeline substantially raises the frequency of stalls.
Each instruction is dependent on previous and proceeds upon data are available, which assumes the pipeline has full bypassing and forwarding.
The SD must be stalled an extra cycle so that its MEM does not conflict with the ADDD. Extra hardware could easily handle this case.
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
LD F4, 0(R2) | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  |  |  | 
MULTD F0, F4, F6 |  | IF | ID | stall | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB |  |  |  | 
ADDD F2, F0, F8 |  |  | IF | stall | ID | stall | stall | stall | stall | stall | stall | A1 | A2 | A3 | A4 | MEM | WB
SD 0(R2), F2 |  |  |  |  | IF | stall | stall | stall | stall | stall | stall | ID | EX | stall | stall | stall | MEM

## Slide 255: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
RAW hazards: Figure: typical FP code sequence showing the stalls arising from RAW hazards.
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17
LD F4, 0(R2) | IF | ID | EX | MEM | WB |  |  |  |  |  |  |  |  |  |  |  | 
MULTD F0, F4, F6 |  | IF | ID | stall | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB |  |  |  | 
ADDD F2, F0, F8 |  |  | IF | stall | ID | stall | stall | stall | stall | stall | stall | A1 | A2 | A3 | A4 | MEM | WB
SD 0(R2), F2 |  |  |  |  | IF | stall | stall | stall | stall | stall | stall | ID | EX | stall | stall | stall | MEM
The forwarding can be implemented by checking if the destination register in any of EX/MEM, A4/MEM, M7/MEM, D(Div)/MEM, or MEM/WB registers is one of the source registers of a floating-point instruction.

## Slide 256: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
WAW hazard: Figure: this hazard only occurs when the result of ADD is overwritten without any instruction ever using it.
Instruction | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11
MULTD F0, F4, F6 | IF | ID | M1 | M2 | M3 | M4 | M5 | M6 | M7 | MEM | WB
 |  | IF | ID | EX | MEM | WB |  |  |  |  | 
 |  |  | IF | ID | EX | MEM | WB |  |  |  | 
ADDD F2, F4, F6 |  |  |  | IF | ID | A1 | A2 | A3 | A4 | MEM | WB
 |  |  |  |  | IF | ID | EX | MEM | WB |  | 
LD F2, 0(R2) |  |  |  |  |  | IF | ID | EX | MEM | WB | 
 |  |  |  |  |  |  | IF | ID | EX | MEM | WB
If LD is issued one cycle earlier and had a destination of F2, then it would create a WAW hazard (write F2 one cycle earlier than ADDD).
If there were use of F2 between ADDD and LD, pipeline need stalled for RAW hazard, and LD would not issue until ADDD was completed.
因此，先解决RAW, WAW可能消失。

## Slide 257: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
WAW hazard: solution.
① delay the issue of load instruction until ADDD enters MEM. 早解决:延缓load发射,直到ADDD进入MEM
② detecting the hazard and changing the control so that the ADDD does not write result. Then, LD can issue right away. 到时候再解决: 检测到冒险,就改变控制,使ADDD不写结果。这样，LD就能立即发射
This hazard is rare (ADDD无用时才出现，ADDD有用时在解决RAW冒险时就顺便解决了), so either scheme work fine.
In either case, detect hazard during ID. Then stalling LD or making ADDD a no-op is easy. 两种情况都在ID检测冒险, 然后阻塞LD和使ADDD不操作就容易了

## Slide 258: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
All the hazards:
Assume: hazard detection is in ID, 3 checks must be performed before issue an instruction:
① Check for structural hazards —Wait until：
the required functional unit isn’t busy (only needed for divides in this pipeline). 等待直至功能单元能用。只有除法器件需要这种检测
make sure the register write port is available when needed. 确保寄存器写端口在需要时能得到
② Check for RAW data hazard —Wait until the source registers not listed as pending destination in the pipeline register that will not be available when this instruction needs the result.
③ Check for WAW data hazard —Determine if any instruction in A1,..., A4, D, M1,..., M7 has the same destination as this instruction.

## Slide 259: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure： the number of stall cycles for each type of floating-point operation on a per instance basis.
Performance of a DLX FP Pipeline DLX浮点流水线的性能
As expected, the stall cycles per operation track the latency of the FP operations, varying from 46% to 59% of the latency of the functional unit.

## Slide 260: 3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Figure： the complete breakdown of integer and floating-point stalls for the five FP SPEC benchmarks.
Performance of a DLX FP Pipeline DLX浮点流水线的性能
There are four classes of stalls shown: FP result stalls, FP compare stalls, load and branch delays, and floating point structural delays.
The total number of stalls per instruction varies from 0.65 to 1.21.
FP result stalls dominate in all cases, with an average of 0.71 stalls per instruction or 82% of the stalled cycles.

## Slide 261: 3.7 Overcoming Data Hazard with Dynamic Scheduling
So far:
no hazard or can forwarding -> issue. 没有冒险, 或者可以前送，则发射
otherwise -> stall, until dependence is cleared. 否则, 阻塞，直至依赖关系解除
compiler techniques -> schedule instructions -> separate dependent instructions and minimize the number of actual hazards and resultant stalls. 编译器技术
This last approach is called static scheduling. 静态调度

## Slide 262: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Dynamic scheduling (动态调度策略)
The hardware rearranges the instruction execution to reduce the stalls.
Advantages:
handle cases when dependences are unknown at compile time, and it simplifies the compiler. 能处理在编译时不知道的依赖关系, 简化了编译器
it also allows code that was compiled with one pipeline to run efficiently on a different pipeline. 使得在一个流水线上编译的代码, 在另一个流水线上也能高效运行
Disadvantages:
these advantages are gained at a cost of a significant increase in hardware complexity.

## Slide 263: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Comparisons：
Dynamic scheduling: cannot remove true data dependences, it tries to avoid stalling when dependences are present. 不是消除数据依赖关系, 而是在存在依赖关系时试图避免阻塞
Static scheduling: tries to separate dependent instructions so that they won’t lead to hazards. 试图分开依赖的指令, 使得不会导致冒险
Certainly, static scheduling can also be used on code run on dynamically scheduled pipeline. 两者可一起使用

## Slide 264: 3.7 Overcoming Data Hazard with Dynamic Scheduling
So far -> in-order issue: If an instruction is stalled, no later instructions can proceed. 指令有序发射
For example, consider:
            DIVD F0, F2, F4
            ADDD F10, F0, F8
            SUBD F12, F8, F14
SUBD cannot execute because dependence of ADDD on DIVD causes pipeline to stall; but SUBD is not dependent on anything in pipeline. ADDD因与DIVD相关而阻塞, SUBD虽与之无关也被阻
Dynamic Scheduling: The Idea 动态调度的思想

## Slide 265: 3.7 Overcoming Data Hazard with Dynamic Scheduling
We want instructions to execute as soon as their data operands are available. 希望一但得到操作数, 指令就执行
Thus, pipeline will do out-of-order execution, which implies out-of-order completion. 乱序执行,乱序结束
In introducing out-of-order execution, we split ID into two stages
① Issue — Decode instructions, check for structural hazards.
② Read operands — Wait until no data hazards, then read operands.
Dynamic Scheduling: The Idea 动态调度的思想

## Slide 266: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Instruction fetch后接issue: fetch either into a single-entry latch or into a queue; instructions are then issued from the latch or queue. Fetch将指令读到锁存器或队列中, 然后从那里发射
EX前接read operands: As in DLX FP pipeline, execution may take multiple cycles. When an instruction begins execution and when an instruction completes execution; between the two times, the instruction is in execution
Dynamic Scheduling: The Idea 动态调度的思想

## Slide 267: 3.7 Overcoming Data Hazard with Dynamic Scheduling
IBM 360/91 floating-point unit (Robert Tomasulo in 1967).
The IBM/360 architecture had only four double-precision floating-point registers and had long memory accesses and long float-point delays, these fact is a motivation for the Tomasulo approach.
Tomasulo’s scheme combines key elements of scoreboarding scheme with the introduction of register renaming to avoid WAR and WAW hazard.
Another Dynamic Scheduling Approach—The Tomasulo Approach 动态调度的Tomasulo方法

## Slide 268: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Register renaming:
Original code：
DIV.D F0, F2, F4
ADD.D F6, F0, F8
S.D F6, 0(R1)
SUB.D F8, F10, F14
MUL.D F6, F10, F8
ADD.D/SUB.D: 读后写(WAR)
ADD.D/MUL.D: 写后写(WAW)
Code after renaming:
DIV.D F0, F2, F4
ADD.D S, F0, F8
S.D S, 0(R1)
SUB.D T, F10, F14
MUL.D F6, F10, T
加入暂时寄存器S、T
S:消除了ADD.D/MUL.D
T:消除了ADD.D/SUB.D
DIV.D/ADD.D: 写后读(RAW)
SUB.D/MUL.D: 写后读(RAW)

## Slide 269: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The basic structure of a DLX FP unit using Tomasulo’s algorithm include:
Three operations for the FP adder;
Two operations for FP multiplier;
Load data buffers (Six FP loads or memory reference)
Store data buffers (Three FP store)
Four double-precision floating-point registers.
In Tomasulo’s scheme, register renaming is provided by the reservation station, which buffer the operands of instructions waiting to issue, and by the issue logic. WAW and WAR hazards are avoided by functionality provided by reservation stations. WAW和WAR冒险由保留站的功能消除。保留站缓冲待发射指令的操作数.

## Slide 270: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: The basic structure of a DLX FP unit using Tomasulo’s algorithm.

## Slide 271: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Basic idea:
A reservation station fetches and buffers an operand as soon as it is available, eliminating the need to get operand from a register. 只要操作数可用, 保留站就取来并缓冲, 从而避免从寄存器取操作数
Pending instructions designate the reservation station that will provide input. 悬挂的指令指定为其提供操作数的保留站
Finally, when successive writes to a register appear, only the last one is actually used to update the register (WAW)
As instructions are issued, the register specifiers for pending operands are renamed to the names of the reservation station in a process called register renaming (WAR)
More reservation stations than registers -> can eliminate hazards that couldn’t by compiler. 由于保留站比寄存器多，所以能消除编译器不能消除的冒险

## Slide 272: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Basic idea:
The results from the functional units and the memory are sent on a common data bus (CDB) to everywhere except the loader buffer.
In this way all the waiting units can be loaded the results simultaneously.
All buffers and reservation stations have tag fields that are used by the hazard control logic and other buffers and reservation stations.

## Slide 273: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: The basic structure of a DLX FP unit using Tomasulo’s algorithm.

## Slide 274: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The reservation stations hold:
Instructions: have been issued and are awaiting execution at a functional unit.
Operands for the instruction if have already been computed or the source of the operands otherwise.
Information needed to control the instruction once it has begun execution at the unit.
The load buffers and store buffers hold
data or addresses coming from/going to memory.
The FP registers are connected:
By a pair of buses to the functional units
By a single bus to the store buffers.

## Slide 275: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The basic structure of a DLX FP unit using Tomasulo’s algorithm.
FP operations are sent from the instruction unit into a queue when they are issued. 浮点操作在发射时从指令单元进入队列
Reservation stations include the operation and the actual operands, as well as information used for detecting and resolving hazards. 保留站包括操作及操作数, 以及用于检测和解决冒险的信息
Load buffers: hold results of outstanding loads that are waiting for the CDB. Load缓冲器: 装载尚未完成的load的结果, 在等待CDB

## Slide 276: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The basic structure of a DLX FP unit using Tomasulo’s algorithm.
Store buffers: hold destination addresses of outstanding stores waiting for their operands. Store缓冲器: 装载尚未完成store的目标地址, 在等待操作数
All results from either FP units or load unit are put on CDB, which goes to FP register file as well as to reservation stations and store buffers. 所有来自FP单元或load单元的结果都放到CDB上, 从这里去往FP寄存器文件以及保留站和store缓冲器

## Slide 277: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The three steps that an instruction goes through:
          Issue (发射)
          Execute (执行)
          Write result (写结果)

## Slide 278: 3.7 Overcoming Data Hazard with Dynamic Scheduling
① Issue 发射： Get an instruction from the floating-point operation queue
If is a FP operation, issue it if there is an empty reservation station, and send the operands to the reservation station if they are in the registers. 若是FP操作, 且有空的保留站, 就发射。若操作数在寄存器中, 就将其送到保留站。
If the operation is a load or store, it can issue if there is an available buffer. 如果是load或store, 若有缓冲器空间, 就发射
If there is no empty reservation station or empty buffer, then is structural hazard and instruction stalls until a station or buffer is freed. 如果没有空的保留站或空的缓冲器, 则有结构冒险, 指令阻塞直至有保留站或缓冲器被释放
This step also performs renaming of registers (solve WAR,WAW).这个步骤还进行寄存器重命名,以解决WAR和WAW

## Slide 279: 3.7 Overcoming Data Hazard with Dynamic Scheduling
② Execute 执行：
If one or more of the operands is not available, monitor CDB while waiting for it to be computed. 如果有操作数还不能用, 就监视CDB, 等待其被计算出来
When an operand becomes available, it is placed into the corresponding reservation station. 如果有操作数被计算出来, 就放入到相应的保留站中
When both operands are available, execute the operation.当操作数都计算出来,就在功能单元中执行该操作
This step checks for RAW hazards. 检测RAW冒险(由于在操作数可用之前延迟指令的执行, 避免了RAW)

## Slide 280: 3.7 Overcoming Data Hazard with Dynamic Scheduling
③ Write result 写结果：
When the result is available, write it on CDB and from there into the registers, into any reservation stations waiting for it, to any waiting store buffers. 当计算出结果, 就将其写到CDB上, 并由此送入到任何需要它的保留站和store缓冲器中
Note:
First, there is no checking for WAW and WAR hazards. These are eliminated when the register operands are renamed during issue.
Second, the CDB is used to broadcast results rather than waiting on the registers.
Third, the loads and stores are treated as basic functional units.

## Slide 281: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: The basic structure of a DLX FP unit using Tomasulo’s algorithm.

## Slide 282: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Each reservation station has 6 fields:
Op —Operation to perform on source operands S1 and S2.
Qj, Qk —The reservation stations that will produce the corresponding source operand; zero indicates that source operand is already available in Vj or Vk, or is unneeded. 保留站: 产生源操作数. 如果是零, 就指源操作数已能用且在Vj或Vk中,或者不需要操作数
Vj, Vk —The value of the source operands. Only one of the V field or the Q field is valid for each operand. 源操作数的值. 对每个源操作数, V或Q域只有一个有效
Busy—Indicates this reservation station and its functional unit are occupied. 忙标志:指示保留站及其功能单元被占用

## Slide 283: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Register file has a field:
Qi— The number of reservation station that contains the operation whose result should be stored into this register or into memory.
If the value of Qi is blank (or 0), no currently active instruction is computing a result destined for this register or buffer. For a register, this means the value is simply the register contents. 装载保留站号, 其结果将存在这个寄存器或存储器中. 如果Qi是空或零, 则当前没有指令要计算出值并存到该寄存器或缓冲器. 对于寄存器, 就意味着寄存器的内容就是需要的值.

## Slide 284: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Store buffers each has a field:
Qi— The number of reservation station that contains the operation whose result should be stored into this register or into memory.
Vi---holds the value to be stored
Busy --- Indicating when a buffer is available
Address --- Data address
Load buffers each has a field:
Busy --- Indicating when a buffer is available
Address --- Data address

## Slide 285: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Consider the code sequence:
        1. LD F6, 34(R2)
        2. LD F2, 45(R3)
        3. MULTD F0, F2, F4
        4. SUBD F8, F6, F2
        5. DIVD F10, F0, F6
        6. ADDD F6, F8, F2

## Slide 286: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
RAWs:
        1. LD F6, 34(R2)
        2. LD F2, 45(R3)
        3. MULTD F0, F2, F4
        4. SUBD F8, F6, F2
        5. DIVD F10, F0, F6
        6. ADDD F6, F8, F2

## Slide 287: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
WARs:
        1. LD F6, 34(R2)
        2. LD F2, 45(R3)
        3. MULTD F0, F2, F4
        4. SUBD F8, F6, F2
        5. DIVD F10, F0, F6
        6. ADDD F6, F8, F2

## Slide 288: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Instruction status:
Instruction | Issue | Execute | Write result
LD F6, 34(R2) | √ | √ | √
LD F2, 45(R3) | √ | √ | 
MULTD F0, F2, F4 | √ |  | 
SUBD F8, F6, F2 | √ |  | 
DIVD F10, F0, F6 | √ |  | 
ADDD F6, F8, F2 | √ |  | 

## Slide 289: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Name | Busy | Op | Vj | Vk | Qj | Qk
Add1 | Yes | SUB | Mem[34+Regs[R2]] |  |  | Load2
Add2 | Yes | ADD |  |  | Add1 | Load2
Add3 | No |  |  |  |  | 
Mult1 | Yes | MULT |  | Regs[F4] | Load2 | 
Mult2 | Yes | DIV |  | Mem[34+Regs[R2]] | Mult1 | 
Registers status:
Field | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
Qi | Mult1 | Load2 |  | Add2 | Add1 | Mult2 |  |  | 
Reservation stations:

## Slide 290: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Numbers appended to names add, mult, and load stand for tag for that reservation station.
All instructions have issued, but only first load instruction has completed and written result to CDB
Instruction status table: not a part of hardware, included for help understanding; state of each operation issued is kept in reservation station.
Vj and Vk fields show the value of an operand.
Load and store buffers are not shown.
Load buffer 2 is the only busy load buffer and it is performing on behalf of instruction 2.
An operand is specified by either a Q field or a V field at any time.

## Slide 291: Computer Architecture 计算机体系结构
School of Computer Science and Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 292
Loop: LW R1, 0(R2); load R1 from address 0+R2
ADDI R1, R1 ,#1; R1=R1+1
SW 0(R2), R1; store R1 at address 0+R2
ADDI R2, R2, #4; R2=R2+4
SUB R4, R3, R2; R4=R3-R2
BNEZ R4, Loop; Branch to loop if R4!=0

## Slide 293: 3.7 Overcoming Data Hazard with Dynamic Scheduling
We want instructions to execute as soon as their data operands are available. 希望一但得到操作数, 指令就执行
Thus, pipeline will do out-of-order execution, which implies out-of-order completion. 乱序执行,乱序结束
In introducing out-of-order execution, we split ID into two stages
① Issue — Decode instructions, check for structural hazards.
② Read operands — Wait until no data hazards, then read operands.
Dynamic Scheduling: The Idea 动态调度的思想

## Slide 294: 3.7 Overcoming Data Hazard with Dynamic Scheduling
IBM 360/91 floating-point unit (Robert Tomasulo in 1967).
The IBM/360 architecture had only four double-precision floating-point registers and had long memory accesses and long float-point delays, these fact is a motivation for the Tomasulo approach.
Tomasulo’s scheme combines key elements of scoreboarding scheme with the introduction of register renaming to avoid WAR and WAW hazard.
Another Dynamic Scheduling Approach—The Tomasulo Approach 动态调度的Tomasulo方法

## Slide 295: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The basic structure of a DLX FP unit using Tomasulo’s algorithm include:
Three operations for the FP adder;
Two operations for FP multiplier;
Load data buffers (Six FP loads or memory reference)
Store data buffers (Three FP store)
Four double-precision floating-point registers.
In Tomasulo’s scheme, register renaming is provided by the reservation station, which buffer the operands of instructions waiting to issue, and by the issue logic. WAW and WAR hazards are avoided by functionality provided by reservation stations. WAW和WAR冒险由保留站的功能消除。保留站缓冲待发射指令的操作数.

## Slide 296: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The three steps that an instruction goes through:
          Issue (发射)
          Execute (执行)
          Write result (写结果)

## Slide 297: 3.7 Overcoming Data Hazard with Dynamic Scheduling
① Issue 发射： Get an instruction from the floating-point operation queue
If is a FP operation, issue it if there is an empty reservation station, and send the operands to the reservation station if they are in the registers. 若是FP操作, 且有空的保留站, 就发射。若操作数在寄存器中, 就将其送到保留站。
If the operation is a load or store, it can issue if there is an available buffer. 如果是load或store, 若有缓冲器空间, 就发射
If there is no empty reservation station or empty buffer, then is structural hazard and instruction stalls until a station or buffer is freed. 如果没有空的保留站或空的缓冲器, 则有结构冒险, 指令阻塞直至有保留站或缓冲器被释放
This step also performs renaming of registers (solve WAR,WAW).这个步骤还进行寄存器重命名,以解决WAR和WAW

## Slide 298: 3.7 Overcoming Data Hazard with Dynamic Scheduling
② Execute 执行：
If one or more of the operands is not available, monitor CDB while waiting for it to be computed. 如果有操作数还不能用, 就监视CDB, 等待其被计算出来
When an operand becomes available, it is placed into the corresponding reservation station. 如果有操作数被计算出来, 就放入到相应的保留站中
When both operands are available, execute the operation.当操作数都计算出来,就在功能单元中执行该操作
This step checks for RAW hazards. 检测RAW冒险(由于在操作数可用之前延迟指令的执行, 避免了RAW)

## Slide 299: 3.7 Overcoming Data Hazard with Dynamic Scheduling
③ Write result 写结果：
When the result is available, write it on CDB and from there into the registers, into any reservation stations waiting for it, to any waiting store buffers. 当计算出结果, 就将其写到CDB上, 并由此送入到任何需要它的保留站和store缓冲器中
Note:
First, there is no checking for WAW and WAR hazards. These are eliminated when the register operands are renamed during issue.
Second, the CDB is used to broadcast results rather than waiting on the registers.
Third, the loads and stores are treated as basic functional units.

## Slide 300: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: The basic structure of a DLX FP unit using Tomasulo’s algorithm.

## Slide 301: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Each reservation station has 6 fields:
Op —Operation to perform on source operands S1 and S2.
Qj, Qk —The reservation stations that will produce the corresponding source operand; zero indicates that source operand is already available in Vj or Vk, or is unneeded. 保留站: 产生源操作数. 如果是零, 就指源操作数已能用且在Vj或Vk中,或者不需要操作数
Vj, Vk —The value of the source operands. Only one of the V field or the Q field is valid for each operand. 源操作数的值. 对每个源操作数, V或Q域只有一个有效
Busy—Indicates this reservation station and its functional unit are occupied. 忙标志:指示保留站及其功能单元被占用

## Slide 302: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Register file has a field:
Qi— The number of reservation station that contains the operation whose result should be stored into this register or into memory.
If the value of Qi is blank (or 0), no currently active instruction is computing a result destined for this register or buffer. For a register, this means the value is simply the register contents. 装载保留站号, 其结果将存在这个寄存器或存储器中. 如果Qi是空或零, 则当前没有指令要计算出值并存到该寄存器或缓冲器. 对于寄存器, 就意味着寄存器的内容就是需要的值.

## Slide 303: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Data structures used to detect and eliminate hazards
Store buffers each has a field:
Qi— The number of reservation station that contains the operation whose result should be stored into this register or into memory.
Vi---holds the value to be stored
Busy --- Indicating when a buffer is available
Address --- Data address
Load buffers each has a field:
Busy --- Indicating when a buffer is available
Address --- Data address

## Slide 304: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The major advantages of Tomasulo scheme:
① Distribution of hazard detection logic.
② Eliminate stalls for WAW and WAR hazards.
① Distribution of hazard detection logic: arises from the distributed reservation stations and the use of the CDB.
    if multiple instructions waiting a result
    each already has other operand
    then instructions can be released simultaneously
    by broadcast on the CDB.

## Slide 305: 3.7 Overcoming Data Hazard with Dynamic Scheduling
② WAW and WAR are eliminated by:
(a) renaming registers using reservation stations.
(b) storing operands into reservation station as soon as available.
In the above figure, issued DIVD and ADDD, though WAR hazard involving F6.
1st: if instruction providing value for DIVD has completed, Vk will store result, allowing DIVD to execute independent of ADDD.
2nd: if LD not completed, Qk would be Load1, DIVD would be independent of ADDD.
So in either case, ADDD can issue and executing

## Slide 306: 3.7 Overcoming Data Hazard with Dynamic Scheduling
The major drawback of Tomasulo scheme:
① The complexity of the Tomasulo scheme, which requires a large amount of hardware.
② Lastly, the performance gain is limited by the single completion bus (CDB). While additional CDBs can be added, each CDB must interact with all the pipeline hardware, including the reservation stations.

## Slide 307: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Summary of Tomasulo:
In Tomasulo’s scheme two different techniques are combined:
The renaming of registers to a larger virtual set of registers (by the reservation station). 用更大量虚拟的寄存器(即保留站)对寄存器进行重命名
The buffering of source operands from the register file. 对来自寄存器的源操作数进行缓冲

## Slide 308: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Assume latencies for FP units: Add=2 cycles, multiply=10 cycles, divide= 40 cycles.
Consider the code sequence:
        1. LD F6, 34(R2)
        2. LD F2, 45(R3)
        3. MULTD F0, F2, F4
        4. SUBD F8, F6, F2
        5. DIVD F10, F0, F6
        ADDD F6, F8, F2
        Show what the status tables look like when the MULTD is ready to write its result ?

## Slide 309
Cycle 1
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 |  | 
LD F2, 45(R3) |  |  | 
MULTD F0, F2, F4 |  |  | 
SUBD F8, F6, F2 |  |  | 
DIVD F10, F0, F6 |  |  | 
ADDD F6, F8, F2 |  |  | 
 | Busy | Address
Load 1 | Yes | 34+R2
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | No |  |  |  |  | 
Mult 2 | No |  |  |  |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi |  |  |  | Load 1 |  |  |  | 

## Slide 310
Cycle 2
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 |  | 
LD F2, 45(R3) | 2 |  | 
MULTD F0, F2, F4 |  |  | 
SUBD F8, F6, F2 |  |  | 
DIVD F10, F0, F6 |  |  | 
ADDD F6, F8, F2 |  |  | 
 | Busy | Address
Load 1 | Yes | 34+R2
Load 2 | Yes | 45+R3
Load 3 | No | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi |  | Load2 |  | Load 1 |  |  |  | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | No |  |  |  |  | 
Mult 2 | No |  |  |  |  | 

## Slide 311
Cycle 3
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 
LD F2, 45(R3) | 2 |  | 
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 |  |  | 
DIVD F10, F0, F6 |  |  | 
ADDD F6, F8, F2 |  |  | 
 | Busy | Address
Load 1 | Yes | 34+R2
Load 2 | Yes | 45+R3
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD |  | Regs [F4] | Load 2 | 
Mult 2 | No |  |  |  |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 | Load2 |  | Load 1 |  |  |  | 

## Slide 312
Cycle 4
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 |  | 
DIVD F10, F0, F6 |  |  | 
ADDD F6, F8, F2 |  |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | Yes | 45+R3
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | Yes | SUBD | Mem[34+Regs[R2]] |  |  | Load 2
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD |  | Regs [F4] | Load 2 | 
Mult 2 | No |  |  |  |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 | Load2 |  |  | Add 1 |  |  | 

## Slide 313
Cycle 5
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 |  | 
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 |  |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | Yes | SUBD | Mem[34+Regs[R2]] | Mem[45+Regs[R3]] |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  |  | Add 1 | Mult 2 |  | 

## Slide 314
Cycle 6
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 |  | 
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | Yes | SUBD | Mem[34+Regs[R2]] | Mem[45+Regs[R3]] |  | 
Add 2 | Yes | ADDD |  | Mem[45+Regs[R3]] | Add 1 | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  | Add 2 | Add 1 | Mult 2 |  | 

## Slide 315
Cycle 7
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 | 7 | 
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | Yes | SUBD | Mem[34+Regs[R2]] | Mem[45+Regs[R3]] |  | 
Add 2 | Yes | ADDD |  | Mem[45+Regs[R3]] | Add 1 | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  | Add 2 | Add 1 | Mult 2 |  | 

## Slide 316
Cycle 8
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | Yes | ADDD | SUBD F8, F6, F2 | Mem[45+Regs[R3]] |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  | Add 2 |  | Mult 2 |  | 

## Slide 317
Cycle 9
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 |  | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | Yes | ADDD | SUBD F8, F6, F2 | Mem[45+Regs[R3]] |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  | Add 2 |  | Mult 2 |  | 

## Slide 318
Cycle 10
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 | 10 | 
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | Yes | ADDD | SUBD F8, F6, F2 | Mem[45+Regs[R3]] |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  | Add 2 |  | Mult 2 |  | 

## Slide 319
Cycle 11
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 |  | 
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 | 10 | 11
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  |  |  | Mult 2 |  | 

## Slide 320
Cycle 15
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 | 15 | 
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 | 10 | 11
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULTD | Mem[45+Regs[R3]] | Regs [F4] |  | 
Mult 2 | Yes | DIVD |  | Mem[34+Regs[R2]] | Mult 1 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Mult 1 |  |  |  |  | Mult 2 |  | 

## Slide 321
Cycle 16
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 | 15 | 16
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 |  | 
ADDD F6, F8, F2 | 6 | 10 | 11
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | No |  |  |  |  | 
Mult 2 | Yes | DIVD | MULTD F0, F2, F4 | Mem[34+Regs[R2]] |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi |  |  |  |  |  | Mult 2 |  | 

## Slide 322
Cycle 56
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 | 15 | 16
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 | 56 | 
ADDD F6, F8, F2 | 6 | 10 | 11
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | No |  |  |  |  | 
Mult 2 | Yes | DIVD | MULTD F0, F2, F4 | Mem[34+Regs[R2]] |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi |  |  |  |  |  | Mult 2 |  | 

## Slide 323
Cycle 57
Instruction | Issue | Execute | Write
LD F6, 34(R2) | 1 | 3 | 4
LD F2, 45(R3) | 2 | 4 | 5
MULTD F0, F2, F4 | 3 | 15 | 16
SUBD F8, F6, F2 | 4 | 7 | 8
DIVD F10, F0, F6 | 5 | 56 | 57
ADDD F6, F8, F2 | 6 | 10 | 11
 | Busy | Address
Load 1 | No | 
Load 2 | No | 
Load 3 | No | 
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | No |  |  |  |  | 
Mult 2 | No |  |  |  |  | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi |  |  |  |  |  |  |  | 

## Slide 324: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Instruction status:
Instruction | Issue | Execute | Write result
LD F6, 34(R2) | √ | √ | √
LD F2, 45(R3) | √ | √ | √
MULTD F0, F2, F4 | √ | √ | 
SUBD F8, F6, F2 | √ | √ | √
DIVD F10, F0, F6 | √ |  | 
ADDD F6, F8, F2 | √ | √ | √

## Slide 325: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
Reservation stations:
Name | Busy | Op | Vj | Vk | Qj | Qk
Add1 | No |  |  |  |  | 
Add2 | No |  |  |  |  | 
Add3 | No |  |  |  |  | 
Mult1 | Yes | MULT | Mem[45+Regs[R3]] | Regs[F4] |  | 
Mult2 | Yes | DIV |  | Mem[34+Regs[R2]] | Mult1 | 
Registers status:
Field | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … | F30
Qi | Mult1 |  |  |  |  | Mult2 |  |  | 

## Slide 326: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
ADDD has completed since operands of DIVD are copied, thereby overcoming WAR hazard. 由于DIVD的操作数是拷贝的(load指令的结果), 故ADDD完成, 因而消除了WAR冒险
Even if the load of F6 was delayed, the add into F6 could be executed without WAW hazard. 即使载入F6的操作延迟, ADDD操作也能进行而无WAW冒险
MULT and DIV are only instructions not finished. 只有MULT和DIV指令未完成

## Slide 327: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: The basic structure of a DLX FP unit using Tomasulo’s algorithm.

## Slide 328: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: steps in algorithm and what is required for each step.
Name | Wait until | Action or bookkeeping
Issue | Station or buffer empty | if (Register[‘S1’].Qi≠0) {RS[r].Qj←Register[‘S1’].Qj} else {RS[r].Vj←S1; RS[r].Qj←0}; If (Register[‘S2’].Qi≠0) {RS[r].Qk←Register[‘S2’].Qi} else {RS[r].Vk←S2; RS[r].Qk←0}; RS[r].Busy←Yes; Register[‘D’].Qi=r;
Execute | (RS[r].Qj = 0) and (RS[r].Qk = 0) | None --- operands are in Vj and Vk
Write result | Execution completed at r and CDB Available | 

## Slide 329: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: steps in algorithm and what is required for each step.
For the issuing instruction, D is the destination, S1 and S2 are the source register numbers, and r is the reservation station or buffer that D is assigned to. RS is the reservation-station data structure. 发射: D:目标(即需要这条指令计算结果的寄存器); S1, S2: 源寄存器号; r: 对D赋值的保留站或缓冲器; RS: 保留站的数据结构
The value returned by a reservation station or by the load unit is called result. 保留站或load单元返回的值称为结果(result)
Register is register data structure (not register file), while Store is the store-buffer data structure. Register是寄存器的数据结构, Store是store缓冲器的数据结构
‘Ri’ means name of register Ri, rather than the contents of Ri. ‘Ri’的意思是寄存器Ri, 而不是Ri的内容

## Slide 330: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: steps in algorithm and what is required for each step.
When an instruction is issued, the destination register has its Qi field set to the number of the buffer or reservation station to which the instruction is issued. 当指令发射时, 其目标寄存器的Qi置为该指令的缓冲器或保留站的号
If the operands are available in the registers, they are stored in the V fields. Otherwise, the Q fields are set to indicate the reservation station that will produce the values. 若操作数已在寄存器中, 就将其存到V域中; 否则, 就将Q域设置为产生这个结果的保留站
The instruction waits at the reservation station until both its operands are available, indicated by zero in the Q fields. 保留站中指令等待, 直至其两个操作数都可用(Q域为零).

## Slide 331: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Figure: steps in algorithm and what is required for each step.
When an instruction has finished execution and the CDB is available, it can do its write back. 当指令完成, 并且CDB可用时, 就写回结果
All the buffers, registers, and reservation stations whose value of Qj or Qk is the same as the completing reservation station update their values from the CDB and mark the Q fields to indicate that values have been received. 所有其Qi或Qk与刚完成的保留站相同的缓冲器、寄存器、保留站均从CDB更新其值, 并标记Q域(为零)以指示值已得到.
Thus, the CDB can broadcast its result to many destinations in a single clock cycle, and if the waiting instructions have their operands, they can all begin execution on the next clock cycle. CDB能在一个时钟周期内将其结果广播到很多目标. 那些等待操作数的指令就能在下一个时钟周期开始执行.

## Slide 332: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
        Loop: LD F0, 0(R1)
        MULTD F4, F0, F2
        SD 0(R1), F4
        SUBI R1, R1, #8
        BNEZ R1, Loop;
All branches are taken.
The reservation stations will allow multiple executions of the loop.
The loop is unrolled dynamically by the hardware.

## Slide 333: 3.7 Overcoming Data Hazard with Dynamic Scheduling
Example:
        Loop: LD F0, 0(R1)
        MULTD F4, F0, F2
        SD 0(R1), F4
        SUBI R1, R1, #8
        BNEZ R1, Loop;
All of the instructions in two successive iterations of the loop have issued.
But none has completed.

## Slide 334
Instruction | Iteration | Issue | Execute | Write
LD F0, 0(R1) | 1 | √ | √ | 
MULTD F4, F0, F2 | 1 | √ |  | 
SD 0(R1), F4 | 1 | √ |  | 
LD F0, 0(R1) | 2 | √ | √ | 
MULTD F4, F0, F2 | 2 | √ |  | 
SD 0(R1), F4 | 2 | √ |  | 
Field | Load1 | Load2 | Load3
Add | Regs[R1] | Regs[R1]-8 | 
Busy | Yes | Yes | No
Name | Busy | Op | Vj | Vk | Qj | Qk
Add 1 | No |  |  |  |  | 
Add 2 | No |  |  |  |  | 
Add 3 | No |  |  |  |  | 
Mult 1 | Yes | MULT |  | Regs[F2] | Load1 | 
Mult 2 | Yes | MULT |  | Regs[F2] | Load2 | 
Instruction status
Reservation stations
Register result status
 | F0 | F2 | F4 | F6 | F8 | F10 | F12 | … F30
Qi | Load2 |  | Mult2 |  |  |  |  | 
Field | Store1 | Store2 | Store3
Add | Regs[R1] | Regs[R1]-8 | 
Busy | Yes | Yes | No
Qi | Mult1 | Mult2 | 
Load & Store buffer

## Slide 335: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Static: the action taken does not depend on the dynamic behavior of branch. 静态: 采取的动作不取决于转移的动态行为
Dynamic: using hardware, dynamically predict outcome of branch—branch behavior changes, then prediction will change. 用硬件, 动态预测转移的结果. 转移行为改变, 则预测改变
Here we will：
propose a simple branch prediction scheme, then examine approaches that increase accuracy.
look at more elaborate schemes that try to find the instruction following a branch even earlier.

## Slide 336: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Branch prediction buffer or branch history table: the simplest dynamic branch-prediction scheme. 分支预测缓冲器或转移历史表: 最简单的动态转移预测方案
A branch-prediction buffer: A small memory indexed by the lower portion of the address of branch instruction. 用转移指令的低地址部分所索引的一小块存储区
① A one-bit prediction scheme: memory contains a bit that saying whether the branch was recently taken or not. 位: 表示最近该转移是否发生
Basic Branch Prediction and Branch Prediction Buffers
基本转移预测和转移预测缓冲器

## Slide 337: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: The states in a one-bit prediction scheme.
A performance shortcoming of one-bit prediction scheme : Even if a branch is almost always taken ,we will likely predict incorrectly twice, rather than once, when it is not taken.

## Slide 338: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Example: consider a loop branch, taken 9 times, then not taken once. What is prediction accuracy ?
Answer:
The steady-state prediction behavior will mispredict on first and last loop iterations.
for last iteration: inevitable since bit says taken.最后一次预测错误: 不可避免
for first iteration: happens because bit is flipped by the last iteration of the last loop (not taken). 第一次预测错误: 出现的原因是上一个循环最后一次没有成功, 从而使位被翻转
Thus, the prediction accuracy is only 80%.

## Slide 339: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
② 2-bit prediction scheme: a prediction must miss twice before it is changed.错两次才改变预测
Figure: the finite-state processor for a 2-bit prediction scheme.
Successive branches that strongly favors taken or not taken (often cases) will be mispredicted only once.

## Slide 340: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Example:
ADDI R1, R0, #10
Loop: SUBI R3, R1, #1
SUBI R1, R1, #1
BNEZ R1, Loop
A: 1/10; B: 2/10; C: 1/9; D:2/9

## Slide 341: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
③ n-bit prediction scheme:
The two-bit scheme is actually a specialization of a more general scheme that has an n-bit saturating counter for each entry in the prediction buffer.
With n-bit, counter can take between 0 and 2n–1: when  (2n–1)/2, branch is predicted as taken; otherwise, untaken. 计数器可取值0到2n-1. 当  (2n–1)/2时, 预测转移; 否则, 预测不转移
Counter: incremented when branch is taken, and decremented when untaken. 计数器: 转移时递增, 不转移时递减
Studies show: 2-bit predictors do almost as well, thus most systems use 2-bit predictors. 2位预测器就已经很好了, 因此多数系统用2位预测器

## Slide 342: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: Prediction accuracy of a 4096-entry two-bit prediction buffer for the SPEC89 benchmarks. (82%--99%)

## Slide 343: Computer Architecture 计算机体系结构
School of Computer Science and Technology Beijing Jiaotong Univeristy
Yi Tian

## Slide 344: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Branch prediction buffer or branch history table: the simplest dynamic branch-prediction scheme. 分支预测缓冲器或转移历史表: 最简单的动态转移预测方案
A branch-prediction buffer: A small memory indexed by the lower portion of the address of branch instruction. 用转移指令的低地址部分所索引的一小块存储区
① A one-bit prediction scheme: memory contains a bit that saying whether the branch was recently taken or not. 位: 表示最近该转移是否发生
Basic Branch Prediction and Branch Prediction Buffers
基本转移预测和转移预测缓冲器

## Slide 345: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: The states in a one-bit prediction scheme.
A performance shortcoming of one-bit prediction scheme : Even if a branch is almost always taken ,we will likely predict incorrectly twice, rather than once, when it is not taken.

## Slide 346: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
② 2-bit prediction scheme: a prediction must miss twice before it is changed.错两次才改变预测
Figure: the finite-state processor for a 2-bit prediction scheme.
Successive branches that strongly favors taken or not taken (often cases) will be mispredicted only once.

## Slide 347: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
A branch-prediction buffer can be implemented:
A small, special “cache” accessed with the instruction address during the IF pipe stage.
A pair of bits attached to each block in the instruction cache and fetched with the instruction.
This scheme is useful to reduce the branch delay when it is longer than the time to compute the possible target PCs.
This scheme dose not help for the simple DLX pipeline : the DLX pipeline find out both whether the branch is taken and what the target of the branch is at the same time.

## Slide 348: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
The two-bit predictor schemes use only the recent behavior of a branch to predict the future behavior of that branch.
It may be possible to improve the prediction accuracy if we also look at the recent behavior of other branches rather than just the branch we are trying to predict
Branch predictors that use the behavior of other branches to make a prediction are called correlating predictors or two-level predictors.

## Slide 349: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Example: Assuming that aa and bb are assigned to R1 and R2
If (aa==2) aa=0; If (bb==2) bb=0; If (aa!=bb)

## Slide 350: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Example: assuming that d is assigned to R1.
If (d==0)
d=1;
If (d==1)
Assuming that d has values 0,1, and 2.

## Slide 351: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: Possible execution sequences for a code fragment.
Initial value of d | d == 0? | Branch b1 | Value of d before b2 | d == 1? | Branch b2
0 | Yes | Not taken | 1 | Yes | Not taken
1 | No | Taken | 1 | Yes | Not taken
2 | No | Taken | 2 | No | Taken
If (d==0)
d=1;
If (d==1)

## Slide 352: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: Possible execution sequences for a code fragment.
Initial value of d | d == 0? | Branch b1 | Value of d before b2 | d == 1? | Branch b2
0 | Yes | Not taken | 1 | Yes | Not taken
1 | No | Taken | 1 | Yes | Not taken
2 | No | Taken | 2 | No | Taken
Figure: Behavior of one-bit predictor initialized to not taken.
d=? | b1 prediction | b1 action | New b1 prediction | b2 prediction | b2 action | New b2 prediction
2 | NT (initialized) | T | T | NT (initialized) | T | T
0 | T | NT | NT | T | NT | NT
2 | NT | T | T | NT | T | T
0 | T | NT | NT | T | NT | NT

## Slide 353: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Consider a predictor that uses one bit of correlation.
Every branch has two separate prediction bits:
one prediction assuming the last branch executed was not taken.
another prediction assuming the last branch executed was taken.
The one-bit predictor with one bit of correlation uses the behavior of the last branch to choose from among a pair of one-bit branch predictors.

## Slide 354: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
We write the pair of prediction bits together:
The first bit being the prediction if the last branch in the program is not taken.
The second bit being the prediction if the last branch in the program is taken.
Figure: Combinations and meaning of the taken/not taken prediction bits.
This branch Prediction bits | Prediction if last branch no taken | Prediction if last branch taken
NT/NT | Not taken | Not taken
NT/T | Not taken | Taken
T/NT | Taken | Not taken
T/T | Taken | Taken

## Slide 355: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Initial value of d | d == 0? | Branch b1 | Value of d before b2 | d == 1? | Branch b2
0 | Yes | Not taken | 1 | Yes | Not taken
1 | No | Taken | 1 | Yes | Not taken
2 | No | Taken | 2 | No | Taken
Figure: The action of the one-bit predictor with one bit of correlation.
d=? | Branch b1 prediction | b1 action | New b1 prediction | Branch b2 prediction | b2 action | New b2 prediction
2 | NT/NT (initialized) | T | T/NT | NT/NT (initialized) | T | NT /T
0 | T/ NT | NT | T/NT | NT /T | NT | NT /T
2 | T /NT | T | T/NT | NT/ T | T | NT /T
0 | T/ NT | NT | T/NT | NT/ T | NT | NT /T

## Slide 356: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
A (1,1) predictor uses the behavior of the last 1 branch to choose from 21 branch predictors, each of which is a 1-bit predictor for a single branch.
In the general case , a (m,n) predictor uses the behavior of the last m branches to choose from 2m branch predictors, each of which is a n-bit predictor for a single branch.
The simplicity of the hardware comes from a simple observation: The global history of the most recent m branches can be recorded in an m-bit shift register, where each bit records whether the branch was taken or not taken.
The (m,n) branch-prediction buffer can then be indexed using a concatenation of the low-order bits from the branch address with the m-bit global history.

## Slide 357: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: A (2,2) branch-prediction buffer uses a two-bit history to choose from among four predictors for each branch address.

## Slide 358: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
A two-bit predictor with no global history is simply a (0,2) predictor.
The number of bits in a (m,n) predictor =
2m n number of prediction entries selected by the branch address
Example: How many branch-selected entries are in a (2,2) predictor that has a total of 8K bits in the prediction buffer?
Answer:
So, number of prediction entries selected by the branch address is 1K
8K=
22 2 number of prediction entries selected by the branch address

## Slide 359: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
To reduce branch penalty on DLX, we need to know from what address to fetch by end of IF. 为进一步降低转移惩罚, 需要在IF末知道取指地址
This means we must know:
① whether yet-undecoded instruction is a branch. 还没有解码的指令是不是转移指令
② if so, what the next PC should be.
Branch-target buffer or branch-target cache: A branch-prediction cache that stores predicted address for the next instruction after branch. 转移目标缓冲器: 存储所预测的转移后下条指令的地址。
Further Reducing Control Stalls: Branch-Target Buffers
进一步降低控制停顿---转移目标缓冲器

## Slide 360: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
For standard DLX pipeline, branch-prediction buffer is accessed during the ID cycle, so that at end of ID we know the branch-target address (computed during ID), the fall-through address (computed during IF), and the prediction. Thus, by the end of ID we know enough to fetch the next predicted instruction. 转移预测缓冲器: 在ID阶段访被问。在ID末才知道转移目标地址, 不转移时的地址, 以及预测结果。才能取出预测的下一条指令。
For branch-target buffer, we access the buffer during IF using address of fetched instruction (a possible branch) to index the buffer. If hit, we know predicted address at end of IF, 1 cycle earlier than a branch-prediction buffer. 转移目标缓冲器: 在IF用取来指令的地址访问缓冲器。若命中, 就能在IF末知道预测地址, 比转移预测缓冲器早一个周期

## Slide 361: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: A branch-target buffer.
取指指令的PC
查找
预测的PC
入口数
未找到: 非预测为转移的指令,
继续正常进行
找到: 预测为转移,
预测的PC为下一个PC

## Slide 362: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: A branch-target buffer.
The PC of instruction being fetched is matched against a set of addresses stored in first column; these represent the addresses of known branches. 被取来指令的PC与存储在第一列的一组地址(是一些已知的转移地址)进行匹配
If the PC matches one, then the instruction being fetched is taken branch, and second field, predicted PC, contains prediction for next PC after branch. Fetching begins immediately at that address. 如果匹配一个, 则正被取指的指令就被预测为一个成功的转移, 第二个域就包含着转移后的下一个PC, 取指就立即在那里进行
The third field, which is optional, may be used for extra prediction state bits. 第三个域可选, 可用于额外的预测状态位

## Slide 363: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Note that (unlike a branch-prediction buffer) the entry must be for this instruction, because the predicted PC will be sent out before it is known whether this instruction is even a branch. If we did not check whether the entry matched this PC, then the wrong PC would be sent out for instruction that were not branches, resulting in a slower processor
We only need to store the predicted-taken branches in the branch-target buffer, since an untaken branch follows same strategy (fetch the next sequential instruction) as a nonbranch. 在转移目标缓冲器中, 只需存储预测为成功转移的转移，因为未成功的转移遵循与非转移指令相同的策略(即取下一条指令)。

## Slide 364: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: steps followed when using a branch-target buffer.
将PC送到转移目标缓冲器
未找到
找到
查找
否
是
找到预测的PC
正常指令执行
将转移指令地址连同下一个PC送到转移目标缓冲器中
转移成功吗？
否
是
预测错,重取指,删除此入口
预测对,
无阻塞
成功转移吗？

## Slide 365: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Figure: To evaluate branch-target buffer, we must determine penalties in all possible cases.
Instruction in buffer | Prediction | Actual branch | Penalty cycles
Yes | Taken | Taken | 0
Yes | Taken | Not Taken | 2
No |  | Taken | 2
No |  | Not Taken | 0

## Slide 366: 3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Example:
Determine total branch penalty for branch-target buffer, assuming the penalty cycles for individual mis-predictions from the above figure, and
prediction accuracy is 90%
hit rate in the buffer is 90%
taken branch frequency is 60%
Answer:
Branch penalty
= 缓冲器命中率  预测错误率  2
+ (1-缓冲器命中率)分支指令频率2
= Percent buffer hit rate  percent incorrect predictions  2
+(1-percent buffer hit rate)  Taken branches  2
= (90% 10%2) + (10%60%2)
= 0.18 + 0.12 = 0.30 clock cycles

## Slide 367: 3.9 Taking Advantage of More ILP with Multiple Issue
Previously ideal CPI=1. 理想CPI=1; 但是,能使CPI<1吗？能, 采用多发射
Multiple-issue processors: allow multiple instructions to issue in 1 cycle. Two kinds: 多发射处理器: 允许在一个周期发射多条指令. 有两类:
① superscalar processors 超标量处理器
issue varying numbers of instructions per clock. 每个周期发射不同数量的指令
may be either statically scheduled by compiler or dynamically scheduled using Tomasulo’s. 可用编译器进行静态调度, 或者采用Tomasulo进行动态调度
② VLIW (very long instruction word) processors 超长指令字处理器
issue a fixed number of instructions formatted as 1 large instruction(fixed instruction packet). 发射固定数量的指令, 格式化成一个大指令(固定指令包)
inherently statically scheduled by the compiler. 用调度器进行静态调度

## Slide 368: 3.9 Taking Advantage of More ILP with Multiple Issue
Superscalar processor: hardware might issue from 1 to 8 instructions in a clock cycle. 硬件可在单周期发射1到8条指令
these instructions must be independent and satisfy some constraints (example: no more than 1 memory reference issued per clock). 这些指令必须独立, 并满足一些约束(例如: 每个周期不能发射多于一次的存储器访问)
If not, only the instructions preceding that one in sequence will be issued, hence the variability in issue rate. 否则, 只能发射那条指令前面的指令, 因此发射率是变化的
A Superscalar Version of DLX DLX的超标量形式

## Slide 369: 3.9 Taking Advantage of More ILP with Multiple Issue
Let’s assume that two instruction can be issued per clock cycle in DLX processor. One of the instruction can be a load, store, branch, or integer ALU operation , and the other can be any floating-point operation
The instructions be paired and aligned on a 64-bit boundary, with the integer portion appearing first.
The second instruction can be issued only if the first instruction can be issued.
A Superscalar Version of DLX DLX的超标量型式

## Slide 370: 3.9 Taking Advantage of More ILP with Multiple Issue
Figure: Superscalar pipeline in operation.
Instruction type | Pipe stages |  |  |  |  |  |  | 
Integer instruction | IF | ID | EX | MEM | WB |  |  | 
FP instruction | IF | ID | EX | MEM | WB |  |  | 
Integer instruction |  | IF | ID | EX | MEM | WB |  | 
FP instruction |  | IF | ID | EX | MEM | WB |  | 
Integer instruction |  |  | IF | ID | EX | MEM | WB | 
FP instruction |  |  | IF | ID | EX | MEM | WB | 
Integer instruction |  |  |  | IF | ID | EX | MEM | WB
FP instruction |  |  |  | IF | ID | EX | MEM | WB

## Slide 371: 3.9 Taking Advantage of More ILP with Multiple Issue
The only difficulties: When the integer instruction is a floating-point load, store, or move. This creates contention for the floating-point register ports and may also create a new RAW hazard when FP operation is dependent on the first instruction of the pair. 当整数指令是一个浮点load, store,或者move, 就会对FP寄存器端口产生竞争,并且当FP操作依赖指令对的前一条指令时会产生新的RAW冒险
There is another difficultly that may limit the effectiveness of a superscalar pipeline. Loads had a latency of one clock cycle. In the superscalar pipeline, the result of a load instruction cannot be used on the same clock cycle or on the next clock cycle. This means that the next three instructions cannot use the load result without stalling. 由于load指令会额外带来一个周期的延迟，因此会影响配对指令和后续的两条指令，就是影响到了后续的三条指令。

## Slide 372: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：Below is the loop we unrolled and scheduled. How would it be scheduled on a superscalar pipeline for DLX?
Loop: LD F0, 0(R1) ; F0=array element
ADDD F4, F0, F2 ; add scalar in F2
SD 0(R1), F4 ; store result
SUBI R1, R1, #8 ; decrement pointer
BNEZ R1, Loop ; branch R1!=0
Instruction producing result | Instruction using result | Latency in clock cycles
FP ALU op | FP ALU op | 3
FP ALU op | Store double | 2
Load double | FP ALU op | 1
Load double | Store double | 0

## Slide 373: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：Without any Scheduling the loop
Loop: LD F0, 0(R1)
stall
ADDD F4, F0, F2
stall
stall
SD 0(R1), F4
SUBI R1, R1, #8
stall
BNEZ R1, Loop
stall
10 clock cycles per iteration

## Slide 374: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：Schedule the loop to obtain only one stall
Loop: LD F0, 0(R1)
SUBI R1, R1, #8
ADDD F4, F0, F2
stall
BNEZ R1, Loop
SD 8(R1), F4
6 clock cycles per iteration

## Slide 375: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：Before Scheduling:
(17+3*5+2)/5=6.8 clock cycles per iteration

## Slide 376: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：After Scheduling:
17/5=3.4 clock cycles per iteration

## Slide 377: 3.9 Taking Advantage of More ILP with Multiple Issue
Example：The unrolled and scheduled code as it would look on a superscalar DLX:
12/5=2.4 clock cycles per iteration

## Slide 378: 3.9 Taking Advantage of More ILP with Multiple Issue
VLIW packages multiple operations into one very long instruction. VLIW将多个操作打包成一个非常长的指令
Since the burden (choosing instructions to be issued together) falls on compiler, hardware (in superscalar) is unneeded. 由于负担(选择能一起发射的指令)落在了编译器上, 不需要硬件(与超标量不同).
With a VLIW we can reduce the amount of hardware needed to implement a multiple-issue processor.
LIW (long instruction word) or VLIW (very long instruction word) architecture is multiple, independent functional units
The VLIW Approach VLIW方法

## Slide 379: 3.9 Taking Advantage of More ILP with Multiple Issue
A VLIW instruction might include: two integer operations, two FP operations, two memory references, and a branch. 一个VLIW指令可能包括: 两个整数操作, 两个FP操作, 两个存储器访问, 以及一个branch.
An instruction would have a set of fields for each functional unit---perhaps 16 to 24 bit per unit, yielding an instruction length of between 112 and 168 bits.
To keep functional units busy, there must be enough parallelism. 要保持功能单元忙, 就必须有足够的并行性
The parallelism is uncovered by unrolling loops and scheduling code across basic blocks. 并行性通过展开循坏并调度代码来实现

## Slide 380: 3.9 Taking Advantage of More ILP with Multiple Issue
Example:
Suppose: VLIW can issue 2 memory references, 2 FP operations, and 1 integer operation or branch in every clock cycle.
Show an unrolled version of adding a scalar value to an array in memory for such a processor. Unroll as many times as necessary to eliminate any stalls.
Ignore the branch delay slot.
Loop: LD F0, 0(R1) ; F0=array element
ADDD F4, F0, F2 ; add scalar in F2
SD 0(R1), F4 ; store result
SUBI R1, R1, #8 ; decrement pointer
; 8 bytes (per DW)
BNEZ R1, LOOP ; branch R1!=zero

## Slide 381: 3.9 Taking Advantage of More ILP with Multiple Issue
Example :
The loop has been unrolled to make 5 copies of the body, which eliminates all stalls (i.e., completely empty issue cycles), and runs in 8 cycles.
This yields a running rate of 5 results in 8 cycles, or 1.6 cycles per result.
memory reference 1 | memory reference 2 | FP operation 1 | FP operation 2 | Integer operation/branch
LD F0,0(R1) | LD F6,-8(R1) |  |  | 
LD F10,-16(R1) | LD F14,-24(R1) |  |  | 
LD F18,-32(R1) |  | ADDD F4,F0,F2 | ADDD F8,F6,F2 | 
 |  | ADDD F12,F10,F2 | ADDD F16,F14,F2 | 
 |  | ADDD F20,F18,F2 |  | 
SD 0(R1),F4 | SD –8(R1),F8 |  |  | 
SD –16(R1),F12 | SD –24(R1),F16 |  |  | SUBI R1,R1,#40
SD 24(R1),F20 |  |  |  | BNEZ R1,Loop

## Slide 382: 3.9 Taking Advantage of More ILP with Multiple Issue
Example :
The loop has been unrolled to make 7 copies of the body, which eliminates all stalls (i.e., completely empty issue cycles), and runs in 9 cycles.
This yields a running rate of seven results in 9 cycles, or 1.29 cycles per result.
memory reference 1 | memory reference 2 | FP operation 1 | FP operation 2 | Integer operation/branch
LD F0,0(R1) | LD F6,-8(R1) |  |  | 
LD F10,-16(R1) | LD F14,-24(R1) |  |  | 
LD F18,-32(R1) | LD F22,-40(R1) | ADDD F4,F0,F2 | ADDD F8,F6,F2 | 
LD F26,-48(R1) |  | ADDD F12,F10,F2 | ADDD F16,F14,F2 | 
 |  | ADDD F20,F18,F2 | ADDD F24,F22,F2 | 
SD 0(R1),F4 | SD –8(R1),F8 | ADDD F28,F26,F2 |  | 
SD –16(R1),F12 | SD –24(R1),F16 |  |  | SUBI R1,R1,#56
SD 24(R1),F20 | SD 16(R1),F24 |  |  | 
SD 8(R1),F28 |  |  |  | BNEZ R1,Loop

## Slide 383: 3.10 Thread-Level Parallelism （自学）
ILP和TLP: 指令集并行和线程级并行
To achieve high performance, contemporary computer systems rely on two forms of parallelism: instruction-level parallelism (ILP) and thread-level parallelism (TLP).
TLP:
  is inherent in an application that runs multiple threads at once. 同时运行多个线程
  is found largely in applications written for commercial servers such as databases. 商业服务器应用中常见。

## Slide 384: 3.10 Thread-Level Parallelism
A scalar processor processes one data item at a time. A thread is short for a thread of execution.
Threads are a way for a program to split itself into two or more simultaneously (or pseudo- simultaneously) running tasks. 线程：程序将自身分解成多个同时运行的任务的方式
On a single scalar processor, multithreading generally occurs by time-division multiplexing. 在标量处理器上,多线程通常通过时分多路选择实现
Scalar Processor’s Support of Multithreading
标量处理器对多线程的支持

## Slide 385: 3.10 Thread-Level Parallelism
IMT和BMT 交错式多线程和阻塞式多线程
Interleaved multithreading (IMT): an instruction of another thread is fetched and fed into the execution pipeline at each processor cycle.交错式多线程: 在每个处理器周期, 其它线程的指令都被取出并送入执行的流水线
Blocked multithreading (BMT): the instructions of a thread are executed successively until an event occurs that may cause latency. This event induces a context switch. 阻塞式多线程：线程的指令连续执行直至一个会引起延迟的事件发生。

## Slide 386: 3.10 Thread-Level Parallelism
Figure: demonstrates both (a) IMT scalar and (b) BMT scalar.
(a) IMT scalar (b) BMT scalar
Instructions can be issued only from a single thread in a given cycle in a scalar processor, which does not take full advantage of multithreading.

## Slide 387: 3.10 Thread-Level Parallelism
Simultaneous multithreading：SMT
A technique for improving the overall efficiency of superscalar CPUs with hardware multithreading. 采用硬件多线程提高超标量CPU的总体效率的技术
Permits multiple independent threads of execution to better utilize the resources provided by modern processor architectures. 允许多个独立线程执行，以更好地利用现代处理器体系结构所提供的资源
Fig.3.57 demonstrate the support of multithreading with superscalar processors.
Simultaneously Multithreading
同时多线程

## Slide 388: 3.10 Thread-Level Parallelism
Figure: demonstrate the support of multithreading with superscalar processors.
(a) IMT Superscalar (b) BMT Superscalar

## Slide 389: 3.10 Thread-Level Parallelism
3.10.3 Intel Hyper-Threading Technology
超线程技术
3.10.4 Multi-Core Processor Technology
多核技术

## Slide 390: 第三章总结
3.1 What is Pipelining
  Pipelining: is an implementation technique whereby multiple instructions are overlapped in execution.多指令重叠运行。Different steps are completing different parts of different instructions in parallel. 不同步骤并行完成不同指令的不同部分
A Simple Implementation of DLX：IF, ID, EX, MEM, WB.

## Slide 391: 第三章总结
3.2 The Basic Pipeline for DLX
Almost no changes to non-pipeline DLX, just start a new instruction on each clock cycle. 只需在每个时钟周期开始一条新指令
Pipeline registers or pipeline latches: Requires that values passed from one pipe stage to the next must be placed in the registers.

## Slide 392: 第三章总结
3.2 The Basic Pipeline for DLX
Pipeline registers or pipeline latches:

## Slide 393: 第三章总结
3.2 The Basic Pipeline for DLX
Events on every pipes stage of the DLX pipeline

## Slide 394: 第三章总结
3.2 The Basic Pipeline for DLX
Events on every pipes stage of the DLX pipeline
Basic Performance Issues in Pipelining水线的基本性能问题

## Slide 395: 第三章总结
3.3 The Major Hurdle of Pipelining– Pipeline Hazards
Hazards: situations that prevent the next instruction from executing. Hazards reduce performance from the ideal speedup gained by pipelining.
Structural hazards: are resource conflicts, hardware cannot support all possible combinations of instructions in overlapped execution.
Data hazards: an instruction depends on the results of a previous instruction.
Control hazards: arise from the pipelining of branches and other instructions that change PC.

## Slide 396: 第三章总结
3.4 Pipeline Hazards – structural and data hazards
Structural Hazards: If some combination of instructions can not be accommodated because of resource conflicts, the machine is said to have a structural hazard. Why a designer allow structural hazards?
Data Hazard: occur when pipeline changes the order of read/write accesses to operands, so that the order differs from the older seen by sequentially executing instructions on an unpipelined machine.
RAW (read after write) 先写后读
WAW (write after write) 写后再写
WAR (write after read) 先读后写

## Slide 397: 第三章总结
3.5 Pipeline Hazards –Data and control hazard
Data Hazard:
Forwarding.
Data Hazards Requiring Stalls
Compiler Scheduling for Data Hazards
Control Hazard:
① freeze or flush the pipeline
② Treat branch as not taken
③ Treat branch as taken
④ Delayed branch: From before, From target, From fail through

## Slide 398: 第三章总结
3.6 Extending the DLX Pipeline to Handle Multicycle Operations
Hazards and Forwarding in Longer Latency Pipelines:
Structural hazard.
RAW WAW;
3.7 Overcoming Data Hazard with Dynamic Scheduling
Tomasulo
3.8 Reducing Branch Penalties with Dynamic Hardware Prediction
Branch-prediction buffer
Branch-Target Buffers
3.9 Taking Advantage of More ILP with Multiple Issue